## Slide 1: CS2115 Computer Organization 2023/2024 Sem A
Performance Analysis Exercises
Dr. Nan Guan
Department of Computer Science
City University of Hong Kong

## Slide 2: Exercise
We execute a program on a processor
  The processor has separate instruction cache and data cache (1 level)
  Each instruction needs to first load the instruction from the instruction memory to CPU. After that, 15% instructions need to load data from memory to CPU.
  With perfect cache, each instruction executes for 1 CPU cycle .
  Suppose the miss rate of instruction cache is 1%, and the miss rate of data cache is 8%.
  The extra cache miss penalty is 100 cycle
    i.e., in case of a cache miss, 100 cycles are added to the execution time of this instruction
What is the CPI of this program?
  CPI: (average) cycles per instruction

## Slide 3
Suppose the program has X instructions
CPI = Timetotal / X
Timetotal = X * 1 + X * 1% * 100 + X * 15% * 8% * 100
= X (1 + 1 + 1.2)
So CPI = 3.2

## Slide 4: Exercise
We execute a program on a processor
  The processor has a separate level-1 instruction cache and data cache, and a unified level-2 cache
  Each instruction needs to first load the instruction from the instruction memory to the CPU. Then, 20% of instructions need to load data from memory to the CPU.
  With perfect cache, each instruction executes for 1 CPU cycle.
  The total miss rate of level-1 cache is 5%
  The total miss rate of level-2 cache is 1%
  The extra miss penalty is 10 cycle on level-1 cache, and 100 cycles on level-2 cache
What is the speedup if we improve memory access speed by 2 times?
  Level 2 cache miss penalty becomes 50

## Slide 5
Time_old = X + X (120%) 5% * 10 + X (120%) 1% * 5% * 100 = 1.66
Time_new = X + X (120%) 5% * 10 + X (120%) 1% * 5% * 50 = 1.63
Speedup = 1.66/1.63=1.02
Notice: only those memory accesses that are misses on L1 cache will access L2 cache

## Slide 6: Exercise
We execute a program on a processor
  The processor has a separate level-1 instruction cache and data cache, and a unified level-2 cache
  Each instruction needs to first load the instruction from the instruction memory to the CPU. Then, 20% of instructions need to load data from memory to the CPU.
  With perfect cache, each instruction executes for 1 CPU cycle.
  The total miss rate of level-1 cache is 5%
  The total miss rate of level-2 cache is 1%
  The extra miss penalty is 10 cycle on level-1 cache, and 100 cycles on level-2 cache
If you have to either remove level-1 or level-2 cache, which one would you remove?
Notes: Remove L2
Time = X + X (120%) 5% * 100 = 7X
Remove L1
Time = X + X (120%) 100% * 10 + X (120%) 1% * 100 = X + 12X + 1.2X
Should remove L2

## Slide 7
Remove L2
Time = X + X (120%) 5% * 100 = 7X
Remove L1
Time = X + X (120%) 100% * 10 + X (120%) 1% * 100 = X + 12X + 1.2X
Should remove L2

## Slide 8: Exercise
80% of a program can be perfectly parallelized; 10% can be parallelized on at most 4 cores; the remaining has to execute sequentially
What is the speedup if executed on 8 cores?

## Slide 9
Exe_old = x
Exe_new = 0.8 x * 1/8 + 0.1x * ¼ + 0.1 x = 0.225x
X / 0.225x = 4.44

## Slide 10: Exercise
40% of a program can be perfectly parallelized; 40% can be parallelized on at most 8 cores; 10% can be parallelized on at most 4 cores; the remaining has to execute sequentially
To achieve speedup of 4, how many cores are needed at least?
To achieve speedup of 8, how many cores are needed at least?

## Slide 11
(1)
exe_old = x, speedup = 4, so exe_new = 0.25x
Exe_new = 0.4 x / y + 0.4x / min(y,8) + 0.1x / min(y,4) + 0.1 x <= 0.25x
y=7 is the minimal integer satisfying the above inequality

## Slide 12
(2)
exe_old = x, speedup = 8, so exe_new = 0.125x
Exe_new = 0.4 x / y + 0.4x / min(y,8) + 0.1x / min(y,4) + 0.1 x <= 0.25x
Impossible to achieve speedup 8, since no positive y satisfies the above inequality