## Slide 1: CS2115 Computer Organization 2023/2024 Sem A
Chapter 5: CPU
Dr. Nan Guan
Department of Computer Science
City University of Hong Kong

## Slide 2: Overview
Explain the principles and techniques to build a processor
Consider a simple MIPS-like processor example including the following instructions
  Data transfer: lw, sw
  Data operation: add, sub, and, or, slt
    As well as their immediate versions
  Control: beq
  The implementation of other instructions follows the same principle

## Slide 3: Overview
For all types of instructions, the first two steps are identical
  Use PC (program counter) to address the memory that contains the code and fetch the instruction from the memory
  Read one or two registers
    Using fields of the instruction to select registers
    For some instruction (e.g., lw), need to only read one register, but most other instructions read two registers
After these two steps, different instructions do different actions

## Slide 4: Structure of the MIPS Processor
Blue lines: control information
Black lines: data path

## Slide 5: ALU and Auxiliary Computation Logics
ALU
auxiliary computation logics

## Slide 6: Multiplexer
Multiplexer

## Slide 7: Multiplexers
E | S | Y
0 | X | 0
1 | 0 | I0
1 | 1 | I1
S
E
2:1 MUX
(Enable)
Build a 2:1 multiplexer

## Slide 8: Signed Bit Extender
Sign-extend
1100110011001100
11111111111111111100110011001100
0100110011001100
00000000000000000100110011001100

## Slide 9: State Elements
State elements
  PC
  Register
  Memory
Store certain information
Edge-triggered
  All of them have clock inputs
  Emitted here for simplicity
    Note: in reality, the CPU does not directly connect to instruction and data memory, but to caches instead

## Slide 10: Register File
Which registrer to read (as the 1st operand)
Which registrer to read (as the 2nd operand)
Which registrer to write (as the destination)
What data to write into the destination
The data read from register 1
The data read from register 2
Whether read or write
Example: a register file with 8 registers
Write data
read data 1
read data 2
add $s0, $s1, $s2
destination
1st operand
2nd operand

## Slide 11: Decoder
Has an n-bit input and 2n outputs
Only one output is set to 1 for each input combination
    others outputs are 0
Decoder translates the n-bit input into a signal that corresponds to the binary value of the n-bit input

## Slide 12: Fetching Instructions
Simplified view of the part fetching
instruction and incrementing PC
Clock
PC is edge triggered

## Slide 13: Decoding Instructions
opcode
opcode
opcode
add $t3, $t1, $t2
R-type instruction

## Slide 14: Decoding Instructions
opcode
opcode
opcode
add $t3, $t1, $t2
R-type instruction

## Slide 15: Decoding Instructions
opcode
opcode
opcode
add $t3, $t1, $t2
R-type instruction

## Slide 16: Decoding Instructions
opcode
opcode
opcode
add $t3, $t1, $t2
R-type instruction

## Slide 17: Decoding Instructions
opcode
opcode
opcode
add $t3, $t1, $t2
R-type instruction

## Slide 18: Control Logic
opcode
opcode
opcode
add $t3, $t1, $t2
R-type instruction

## Slide 19: Control Logic
Combinational logic
Input (of some bits)
Output (of some bits)

## Slide 20: Control Logic
Combinational logic
Input (of some bits)
Output (of some bits)

## Slide 21: Control Logic
deasserted: 0
asserted: 1

## Slide 22: Control Logic
opcode
opcode
opcode
Used only for shift operations (ignore here)
add $t3, $t1, $t2
R-type instruction
ALU control code

## Slide 23: Execution
opcode
opcode
opcode
add $t3, $t1, $t2
R-type instruction

## Slide 24: add vs. addi
opcode
opcode
opcode
I-type instruction
R-type instruction
addi $t3, $t2, 100
add $t3, $t1, $t2
immediate

## Slide 25: add vs. addi
opcode
opcode
opcode
I-type instruction
R-type instruction
addi $t3, $t2, 100
add $t3, $t1, $t2
immediate

## Slide 26: Load Word
opcode
opcode
opcode
lw $t1, 100($t2)
immediate
I-type instruction
R-type instruction

## Slide 27: Load Word
opcode
opcode
opcode
lw $t1, 100($t2)
immediate
I-type instruction
R-type instruction

## Slide 28: Load Word
opcode
opcode
opcode
lw $t1, 100($t2)
immediate
I-type instruction
R-type instruction

## Slide 29: Load Word
opcode
opcode
opcode
lw $t1, 100($t2)
immediate
I-type instruction
R-type instruction

## Slide 30: Load Word
opcode
opcode
opcode
lw $t1, 100($t2)
immediate
I-type instruction
R-type instruction
The address of memory content to
be loaded is computed by 100 + $t2

## Slide 31: Load Word
opcode
opcode
opcode
lw $t1, 100($t2)
immediate
I-type instruction
R-type instruction
The address of memory content to
be loaded is computed by 100 + $t2

## Slide 32: Store Word
opcode
opcode
opcode
sw $t1, 100($t2)
immediate
I-type instruction
R-type instruction
The address of memory content to
be loaded is computed by 100 + $t2

## Slide 33: Branch If Equal
opcode
opcode
opcode
beq $t1, $t2, 100
immediate
I-type instruction
R-type instruction
if $t1=$t2, jump to PC+4+100*4

## Slide 34: Clock
All the state elements are edge-triggered
  State elements: PC, register, memory
  Either rising or falling edge-triggered
What if we do not use clocks?
  May cause oscillation: the change at output may change the input, then change the output again, and repeat forever and never be stable
So far an instruction is finished in one cycle
  Change triggered at an edge, and all updates finished before the next edge arrives

## Slide 35: Problem of Single-Cycle Processor
In single-cycle processor
  The signal has to pass through many gates in one cycle
  Each gate incurs some delay
  If clock cycle is too short, some updates cannot finish before next edge
Problem 1: even some instructions has very “short” path, it still uses the same clock cycle as those with “long” path
Problem 2: while the signal is propagating through some circuits, other circuits are unused
Single-cycle processor is not used in modern computers
Clock

## Slide 36: Pipeline
Divide instructions into sequential steps (aka "pipeline")
Performed by different processor units with different parts of instructions processed in parallel
Keep every part of the processor busy as much as possible

## Slide 37: Pipeline
In MIPS, instructions are executed in five stages
  IF: instruction fetch stage
  ID: instruction decode & register file read stage
  EX: execution stage
  MEM: memory access stage
  WB: write-back stage
add $s0, $t1, $t2
add $s1, $t3, $t4
add $s2, $t5, $t6

## Slide 38: Pipeline
Implemented by adding pipeline registers between two steps

## Slide 39: Pipeline Hazard
There are situations in pipelining when the next instruction cannot execute in the following clock cycle
Different types of hazard
  Structural hazard
  Data hazard
  Control hazard

## Slide 40: Structural Hazard
lw $1, 100($0)
lw $2, 200($0)
lw $3, 300($0)
lw $4, 400($0)
Occurs when hardware does not support the desired combination of instructions execute in the same clock cycle
Solution: change the hardware
If the memory does not allow to access two different pieces of information (data and instruction) in the same clock cycle, it is a structural hazard

## Slide 41: Data Hazard
Occurs when the pipeline must be stalled because one step must wait for another to complete
  For example, we have an add instruction followed immediately by a subtract instruction that uses the sum ($s0)
sub $t2, #s0, $t3
add $s0, $t0, $t1

## Slide 42: Data Hazard
Occurs when the pipeline must be stalled because one step must wait for another to complete
  For example, we have an add instruction followed immediately by a subtract instruction that uses the sum ($s0)
  The add instruction doesn’t write its result until the fifth stage, so we have to waste three clock cycles in the pipeline – pipline stall
sub $t2, #s0, $t3
add $s0, $t0, $t1

## Slide 43: Forwarding
Solution: Forwarding
  Add extra hardware to retrieve missing information early from the internal resources

## Slide 44: Forwarding

## Slide 45: Data Hazard
Forwarding cannot avoid all pipeline stall

## Slide 46: Data Hazard
We may reorder the code to avoid pipeline stalls

## Slide 47: Data Hazard
We may reorder the code to avoid pipeline stalls

## Slide 48: Control Hazards
Arising from the need to make a decision based on the results of one instruction while others are executing
  We must begin fetching the instruction following the branch on the next clock cycle
  Nevertheless, the pipeline cannot possibly know what the next instruction should be
We can simply stall at each conditional branch, until it becomes clear which is the next instruction
  But it wastes cycles

## Slide 49: Control Hazards
Can add extra circuits to shorten the stall
  E.g., to add hardware to test registers, calculate the branch address, and update the PC during the second stage of the pipeline
  So the next instruction is clear after the second stage
But the pipeline stall would still exist

## Slide 50: Branch Prediction
Computers usually use branch prediction for better performance
A simple approach is to assume branches to be always untaken
  When you’re right, the pipeline proceeds at full speed
  Only when branches are taken does the pipeline stall

## Slide 51: Branch Prediction
Computers usually use branch prediction for better performance
A simple approach is to assume branches to be always untaken
  When you’re right, the pipeline proceeds at full speed
  Only when branches are taken does the pipeline stall

## Slide 52: Branch Prediction
Computers usually use branch prediction for better performance
A simple approach is to assume branches to be always untaken
  When you’re right, the pipeline proceeds at full speed
  Only when branches are taken does the pipeline stall

## Slide 53: Branch Prediction
Computers usually use branch prediction for better performance
A simple approach is to assume branches to be always untaken
  When you’re right, the pipeline proceeds at full speed
  Only when branches are taken does the pipeline stall
It turns out the branch is taken

## Slide 54: Branch Prediction
Computers usually use branch prediction for better performance
A simple approach is to assume branches to be always untaken
  When you’re right, the pipeline proceeds at full speed
  Only when branches are taken does the pipeline stall

## Slide 55: Branch Prediction
Computers usually use branch prediction for better performance
A simple approach is to assume branches to be always untaken
  When you’re right, the pipeline proceeds at full speed
  Only when branches are taken does the pipeline stall

## Slide 56: Branch Prediction
Computers usually use branch prediction for better performance
A simple approach is to assume branches to be always untaken
  When you’re right, the pipeline proceeds at full speed
  Only when branches are taken does the pipeline stall

## Slide 57: Branch Prediction
Computers usually use branch prediction for better performance
A simple approach is to assume branches to be always untaken
  When you’re right, the pipeline proceeds at full speed
  Only when branches are taken does the pipeline stall

## Slide 58: Branch Prediction
Computers usually use branch prediction for better performance
A simple approach is to assume branches to be always untaken
  When you’re right, the pipeline proceeds at full speed
  Only when branches are taken does the pipeline stall

## Slide 59: Branch Prediction Policy
The simplest policy: always assuming a branch is not taken
Dynamic branch prediction: to look up the address of the instruction to see if a branch was taken this instruction was executed in recent past, and, if so, to begin fetching new instructions from the same place as the last time
  Using branch prediction buffer: small memory indexed by the lower portion of the address of the branch instruction
  E.g., using a bit that says whether the branch by this instruction was recently taken or not

## Slide 60: Branch Prediction Policy
1-bit prediction buffer for one instruction -- weakness
  Example: a loop iterates for N times
    Prediction incorrect twice:
      1st iteration: last time some other loop terminates
      Last iteration: inevitable
To remedy this weakness, 2-bit prediction schemes are often used
  a prediction must be wrong twice before it is changed.