## Slide 1
Department of Electrical Engineering
City University of Hong Kong
Prof. Arindam Basu
EE4803: Analog IC Design
Single transistor Circuits

## Slide 2: Outline
Analog Switch
Active Resistor
Current Sink/Source
*With inputs from Phillip Allen’s course at Georgia Tech and Willy Sansen’s book

## Slide 3: Analog Switch
Real world signal  Analog
Processor Digital
From continuous time, continuous amplitude TO discrete time, discrete amplitude

## Slide 4: Analog Switch: ADC use case
From continuous time, continuous amplitude TO discrete time, discrete amplitude
ADC Process
There are mainly two steps involves in the process of conversion. They are
Sampling and Holding (S/H)
Quantizing and Encoding
Sampling and Holding
In Sampling and Holding (S/H), the continuous signal is sampled and held steady for a short period. This removes variations in the input signal that could affect conversion accuracy. The minimum sampling rate must be twice the maximum frequency of the input signal.
Switch

## Slide 5: MOS as a Switch
Control clock = 1  Switch Turns ON
Control clock = 0  Switch Turns OFF
Good switch  RON very low, ROFF very high
β
For ROFF, need to consider sub-threshold equation
K’
β
1
More accurate

## Slide 6: Switch driving capacitor
Choose W large or small?
Choose L large or small?
Time constant τ  RonC
Settling error after “n” time constants 
What is VGS? Which terminal is Source? Voltage on CL is changing..
K’
K’
K’
Assume initial voltage on CL is 0V.

## Slide 7: More accurate analysis

## Slide 8: Switch driving resistor
Need to consider voltage drop due to potential divider 
Need to consider absolute voltage values  What if VIN = 2V? Not sufficient VGS for NMOS to be ON!
Solution is Transmission Gate Switch!

## Slide 9: Switch driving capacitor: Non-idealities
Control clock = 1  Switch Turns ON
Control clock = 0  Switch Turns OFF
Errors caused by:
Clock feedthrough
Charge Injection

## Slide 10: Switch driving capacitor: Non-idealities
Control clock = 1  Switch Turns ON
Control clock = 0  Switch Turns OFF
Errors caused by:
Clock feedthrough
Charge Injection

## Slide 11: Switch Non-idealities: Parasitic Capacitor
Charge Injection
VGS

## Slide 12: Switch Non-idealities: Parasitic Capacitor
Clock Feedthrough
Proportional to
W
LD
LD
Overlap Capacitors (COL)

## Slide 13: Switch Non-idealities: Parasitic Capacitor
Solutions

## Slide 14: Switch Non-idealities: Dynamic Range
Transmission Gate/ Complementary Switch/ N-P Switch
Also solves Clock feedthrough/Charge injection due to usage of opposite polarity of clock for NMOS and PMOS! 
Depends on Vdd

## Slide 15: Switch Non-idealities: Dynamic Range
Low ON resistance is difficult when VDD decreases
(Why attempt to reduce VDD ?  to reduce power dissipation)
Solution  Boosted clock! (Charge pump)

## Slide 16: Outline
Analog Switch
Active Resistor
Current Sink/Source
*With inputs from Phillip Allen’s course at Georgia Tech and Willy Sansen’s book

## Slide 17: Current Sink/Source
Current Source in EE3122  Tail Current Source in Differential Pair

## Slide 18: Active Resistor
(While this shows AC resistor, analog switch shows MOS can be used as DC resistor as well with smaller area)

## Slide 19: Active Resistor: MOS Diode

## Slide 20: Active Resistor: Analog switch

## Slide 21: Active Resistor: Analog switch

## Slide 22: Outline
Analog Switch
Active Resistor
Current Sink/Source
*With inputs from Phillip Allen’s course at Georgia Tech and Willy Sansen’s book

## Slide 23: Current Sink/Source
Current Source in EE3122  Tail Current Source in Differential Pair

## Slide 24: Ideal Current Sink/Source
CKT
VDD
SOURCE
GND
CKT
VDD
SINK
GND

## Slide 25: Ideal Current Mirror: DC Analysis
Current Source in EE3122  Tail Current Source in Differential Pair
Current
reference
Current
mirror
Current
source

## Slide 26: Current Mirror: Early Effect
Current Source in EE3122  Tail Current Source in Differential Pair

## Slide 27: Current Source: AC analysis
Analyze Rout  As expected, it is ro (OR rds)
How to increase Rout?
Increase channel length  Smaller λ
Cascode current source (shown later)

## Slide 28: MOS Current Sink/Source

## Slide 29: MOS Current Sink/Source
NOTE: VG = VDD - VGG
NOTE: VSD = VDD - VD
VD = 0
VD = VDD

## Slide 30: MOS Current Sink/Source: VMIN

## Slide 31: MOS Current Sink/Source: Simulation

## Slide 32: MOS Current Sink/Source: Improvements

## Slide 33: MOS Current Sink/Source: Improvements
+
Vo go = Vo/ro

## Slide 34: Cascode Current Sink: AC
gm,casrds,casrds,bot

## Slide 35: Cascode Current Sink: DC
Remember, condition for saturation
VDS > VGS – VT
OR, VD – VS > VG – VS – VT
OR, VD > VG - VT

## Slide 36: Cascode Current Sink: Bias voltage
Also, need extra bias current  More power dissipation!

## Slide 37: Self-biased Cascode Current Sink
Also, drain voltages of M1 and M2 are matched now!