## Slide 1: EE2000 Logic Circuit Design
Latch and Flip-Flop Circuits

## Slide 2: Outline
7.1 Latch
  Active High
  Active Low
7.2 Flip-Flop (FF)
  - SR-, D-, JK-, T- FFs
7.3 Master-Slave FF
7.4 Edge-Triggered FF
7.5 Synchronous and Asynchronous Inputs

## Slide 3: Two classes of logic circuits
Combinational logic circuit
Previous lectures have been discussed
Sequential logic circuit
Output depends on present input + past history
Memory circuit (previous STATE information) is required

## Slide 4: Sequential logic circuit
Examples
Vending Machine Food/ drink / MTR tickets
Digital counter / clock
Traffic light controller

## Slide 5: Latch
Two cross-coupled inverters have two stable states: “1” and “0”
The state can be reset with input.
0
1

## Slide 6: 7.1 Latch
The output state of a latch is controlled by its excitation input signals
Latch and flip-flop are memory devices and implemented using bistable circuit - its output will remain in either 0 or 1 state

## Slide 7: Latch
SR (set-reset) latch circuit When S (set) is set to 1, the output Q will be set to 1. Likewise, when R (reset) is set to 1, the output Q will be set to 0. It is invalid to set both S and R to 1
Active High Latch
NOR gate implementation

## Slide 8: Latch
S’R’ latch circuit When S’ (set) is set to 1, the output Q will be set to 0. Likewise, when R’ (reset) is set to 1, the output Q will be set to 1. It is invalid to set both S’ and R’ to 1
Active Low Latch
NAND gate implementation

## Slide 9: Latch
Note that the input is active high for NOR gate implementation, whereas the input is active low for NAND gate implementation
  Require a 1 signal to change its state
  Require a 0 signal to change its state

## Slide 10: Drawbacks
If inputs S, R are unstable (or noise), output produces a unstable short pulse
Solution:
Prevention of input noise
Using “Gated Latch”
The latches will enter undefined state for some inputs (e.g. R = S = 1)
Solution:
Prevent R and S set to 1 simultaneously
Using “D Latch”

## Slide 11: 7.2 Flip-Flop (FF)
The state of flip-flop changes on the transition of the clock
Four types of FF SR FF D-type FF JK FF T FF

## Slide 12: Clocked SR FF
C can be presented by a clocked signal. Then the latch with the clocked signal is called Flip-flop
CLK or

## Slide 13
CLK or

## Slide 14: D-type FF
C can be presented by a clocked signal. Inputs R and S are correlated with D but differentiate by a NOT-gate
CLK or

## Slide 15: JK FF
The JK FF is a refinement of the SR FF in that the undetermined state of the SR type is defined in the JK type. Inputs J and K behave like inputs S and R to set and reset (clear) the FF, respectively. The input marked J is for set and the input marked K is reset.
toggle
hold
Reset
Set

## Slide 16: T-type FF
The toggle (T) FF has a clock input which causes the output state changed for each clock pulse if T is in its active state. It is useful in counter design

## Slide 17: Logic symbols of various latch and flip-flops
SR
SR

## Slide 18: 7.3 Master-Slave Flip-Flop
- Master-Slave SR Flip-Flop

## Slide 20
Clk goes to 1, S affects the output of Y (master enabled)
Clk goes to 0, the output of Q is enabled (slave enabled)
Clk goes to 1 again
R goes to 1, Y is 0 (reset enabled)
The new Y is transferred to Q when Clk goes back to 0
Now Clk is 0 (master disabled), so any change in S, R can’t affect Y
S goes to 1, and back to 1, Y set to 1 again
Q follows Y until Clk falls from 1 to 0

## Slide 21: Pulse-Triggered FF
Its behavior depends on: The rising and the period of the pulse remain at high (Y) and the falling edges (Q)
So referred to as pulse-triggered flip-flops

## Slide 23: Master-Slave JK Flip-Flop

## Slide 27: Master-Slave D Flip-Flop

## Slide 28: Master-Slave T Flip-Flop

## Slide 30: Problems
For MSFF, master is enabled during the period of clock pulse is 1
Undesired behavior produced when inputs values of S and R (or J, K, D, T) change at that period
Better solution: Edge-triggered flip-flops

## Slide 31: 7.4 Edge-Triggered Flip-Flop
Use one of the edges of the clock signal to read the input values - either positive or negative transition - triggering edge
The response to the triggering edge at the output of the flip-flop is almost immediate
The flip-flops remains unresponsive to the input change until the next triggering edge

## Slide 32: Triggering Edge

## Slide 33: Positive-Edge-Triggered D FF

## Slide 34: Timing Diagram

## Slide 35: Negative-Edge-Triggered D FF

## Slide 36: Timing Diagram

## Slide 37: Edge-Triggered JK Flip- Flop

## Slide 38: Edge-Triggered T Flip- Flop

## Slide 39: Timing Diagram
PET

## Slide 40: Logic symbols of various edge-triggered flip-flops
SR

## Slide 41: 7.5 Synchronous and Asynchronous Inputs
Inputs of flip-flops are categorized into two types
Synchronous and asynchronous
All inputs to FFs presented so far are synchronous inputs

## Slide 42: Asynchronous Inputs
The output will response to the sync. inputs only if all async. inputs are inactive
Particularly useful for bringing a FF into a desired initial state prior to normal clocked operation
The asynchronous (or direct) inputs usually called - Preset (denoted by PRE) and clear (denoted CLR) - Used to forcibly set and reset the state of flip-flop

## Slide 43: Example

## Slide 44: Example

## Slide 45: Timing Diagram

## Slide 46: Summary
Flip-flips as memory elements - To store the value in Q - One FF can store 1-bit data
Different types of FFs - SR-type, D-type, JK-type, T-type - By controlling the inputs (S, R, D, J, K, T) to change, set, reset or hold the value of Q
Different Triggering Methods - Pulse-triggered - Edge-triggered