## Slide 1: CS2115 Computer Organization 2023/2024 Sem A
Chapter 3: Circuits
Dr. Nan Guan
Department of Computer Science
City University of Hong Kong

## Slide 2: Outline
Combinational logic circuits
Sequential logic circuits

## Slide 3: Logic Circuits
Operate on binary variables
have inputs and outputs
to implement functions of logic variables

## Slide 4: Logic Gates
Logical circuits are implemented using electronic logic gates
Standard logic gates
OR is also called “add”
Truth Table: sets out the functional values of logical expressions on each combination of values of inputs
AND is also called “product”

## Slide 5: Logic Gates
More gates
NAND gate
NOR gate
inversion
inversion

## Slide 6: Logic Gates
Combinational logic circuits
  made up of basic logic gates that are “combined” or connected together to produce more complicated “functions”
Truth Table

## Slide 7: Rules of Binary Logic
Recall: OR  “add”, AND  “product”

## Slide 8: Rules of Binary Logic
Recall: OR  “add”, AND  “product”
w
y
z
w
y
z
=

## Slide 9: Synthesis of Circuit
Designing a logic circuit according to truth table
Use the sum-of-products form
  Product term: includes all inputs, applying NOT to those of value 0
  Sum of all the product terms having output 1
but this much simpler one also works!
Notes: As illustrated in this example, a logic function can be implemented with circuits of different complexities.
It is useful to minimize a logic expression to reduce the cost of the synthesized circuit.

## Slide 10: Simplification of Logic Expression
Use binary logic rules to simplify

## Slide 11: Simplification of Logic Expression
Karnaugh Maps
  Different form of a truth table which enables easier pattern recognition.
  Pictorial method of simplifying Boolean expressions.
  Good for circuit designs with up to 4 variables.

## Slide 12: Karnaugh Maps
Truth Table
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Karnaugh Map
F
0
1
0
1
B
A
0
0
0
0
0
0
1
1
1
1
1
0
1
1
1
0
0
1
1
1
1
1
1
1

## Slide 13: Deriving Expressions from a Karnaugh Map

## Slide 14
A | B | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
Karnaugh Map
0 | 1
0 | 1
F
0
1
0
1
B
A
1
1
1
0
1
A

## Slide 15
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Karnaugh Map
0 | 1
1 | 1
F
0
1
0
1
B
A
1
1
1
A
1
1
B

## Slide 16
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Karnaugh Map
1 | 1
1 | 1
F
0
1
0
1
B
A
1
1
1
1
1

## Slide 17
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Karnaugh Map
1 | 1
1 | 0
F
0
1
0
1
B
A
1
1
0
A
1
0
B

## Slide 18: Karnaugh Maps with 3 Variables

## Slide 19
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0
1
0
1
BC
A
A
BC
00
00
01
01
01
11
11
11
10
10
0
0
0
0
0
00
0
0
1
0
0
0
01
0
0
0
1
1
1
10
1
1
11
1
1
1
0
1
1
1
0
0
1
1
0
1
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1

## Slide 20
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0
1
BC
A
00
01
11
10
0
0
1
1
1
1
1
1
A
1
1
1
1
1
1
1
B
11
10

## Slide 21
0
1
BC
A
00
01
11
10
0
0
1
1
1
1
1
1
A
B
0 | 1 | 1 | 1
0 | 1 | 1 | 1
C
AB
00
01
11
10
0
1

## Slide 22
0 | 1 | 1 | 1
0 | 1 | 1 | 1
C
AB
00
01
11
10
0
1
WRONG!
CORRECT!
B
01
11
11
10
A
1
1
1
1
1
1

## Slide 23
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
1 | 1 | 1 | 1
0 | 0 | 1 | 1
C
AB
00
01
11
10
0
1

## Slide 24
1 | 1 | 1 | 1
0 | 0 | 1 | 1
C
AB
00
01
11
10
0
1
1
1
1
1
0
C
A
1
1

## Slide 25
0 | 0 | 1 | 0
0 | 0 | 1 | 0
C
AB
00
01
11
10
0
1
11
11
A
B

## Slide 26
0
1
BC
A
00
01
11
10
1
0
1
0
1
0
0
1
1
1
1
0
1
1
00
10
00
10
C

## Slide 27
0
1
BC
A
00
01
11
10
0
0
0
0
1
0
0
1
1
1
1
00
10
A
C

## Slide 28: Summary of Grouping Rules
A group must only contain 1s, no 0s
A group can only be horizontal or vertical, not diagonal
A group must contain 2n 1s (1, 2, 4, 8, etc.)
Each group should be as large as possible
Groups may overlap
Groups may wrap around a table
Every 1 must be in at least one group
There should be as few groups as possible

## Slide 29: Karnaugh Maps with 4 Variables

## Slide 30
A | B | C | D | F
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0
1 | 1 | 1 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 0
CD
AB
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10
1
1
1
1
1
1
1
A | B | C | D | F
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 31
0 | 0 | 1 | 0
1 | 1 | 1 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 0
CD
AB
00
01
11
10
00
01
11
10
11
01
1
1
1
1
1
1
1
A
B
11
C
(A
B)
D
01
C
D)

## Slide 32
0 | 0 | 1 | 1
1 | 1 | 0 | 0
0 | 0 | 0 | 0
0 | 0 | 1 | 1
CD
AB
00
01
11
10
00
01
11
10
A
00
01
01
C
01
D
A
D)
1
1
1
1
1
1
11
10
A
D
00
10
(A
D)

## Slide 33
1 | 1 | 1 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 0
1 | 1 | 1 | 1
CD
AB
00
01
11
10
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1

## Slide 34
1 | 1 | 1 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 0
1 | 1 | 1 | 1
CD
AB
00
01
11
10
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
00
10
D
1
A
00
01
B
11
01

## Slide 35: Half Adder
1-bit half adder
Input |  | Output | 
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
B
S
C
A
∑
A
B
+
S
C

## Slide 36: Half Adder
B
S
C
A
∑
B
S
C
A
∑
Half Adder1
Half Adder2
half adder is not able to add carry-out from the previous addition to the next bits
Notes: One of the main drawback of

## Slide 37: Full Adder
Input |  |  | Output | 
A | B | CI | S | CO
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
B
S
CO
A
∑
CI
1-bit full adder
S = A⊕B⊕CI
CO = A·B+ B·CI+A·CI
Notes: This is taken care using the full adder circuit. The full adder circuit consists of three input bits and two output bits. The three inputs to the full adder are A,B and Ci, where A and B are the bits to be added and Ci is the previous carry bit. The outputs are S and Co, where S is the sum bit and Co is the carry bit generated for this sum.
The truth table for the full adder is also shown here. We can see that the output of sum is high whenever there are odd number of high inputs. And Co bit is high if at least 2 or more than 2 inputs are high.

## Slide 38: Full Adder
1-bit full adder circuit
CI
A
B
S
CO
S = A⊕B⊕CI
CO = AB+ BCI+ACI
Notes: Now since we have the Boolean expressions, we can build the adder circuit using Ex-or, OR and AND gates.

## Slide 39: Ripple Carry Adder
B4
S4
A4
CI
∑
B3
S3
A3
CI
∑
B2
S2
A2
CI
∑
B1
S1
A1
CI
∑
CO
CO
CO
CO
C0
C1
C2
C3
C4
4-bit ripple carry adder (RCA)
The sum of position 2 cannot complete until it receives C1 from position 1.
The sum of position 3 cannot complete until it receives C2 from position 2
…
In this way, the carry “ripples” through the circuit from right to left.
A4
A3
A2
A1
B4
B3
B2
B1
+
S4
S3
S2
S1
C4
C1
C2
C3
Notes: With the full adder, it is very easy to construct the adder. Assuming A4A3A2A1 and B4B3B2B1, the circuit diagram of A4A3A2A1 + B4B3B2B1 serial carry adder using the full adder can be constructed by this.
This series method only completes the basic function, but it is completely infeasible in efficiency.

## Slide 40: Carry Look Ahead Adder
A carry look ahead adder contains circuits that determine whether the previous adder stage produce a carry
Produces the “carry” for each stage without having to wait for the carry to ripple through the prior stage
B4
S4
A4
CI
∑
B3
S3
A3
CI
∑
B2
S2
A2
CI
∑
B1
S1
A1
CI
∑
CO
CO
CO
CO
C0
C1
C2
C3
C4
C4
Notes: To eliminate the ripple delay, we want to create look ahead circuits that are only dependent on the system inputs as opposed to the intermediate carry out signals.

## Slide 41: Carry Look Ahead Adder
Input |  |  | Output
Ai | Bi | Ci | Ci+1
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
√
√
√
√
Ai⊕Bi=1 & Ci=1
Ai·Bi=1
Ci+1 = Ai·Bi+ (Ai ⊕ Bi)·Ci
Carry generator
Carry propagator
G
P
Ci+1 = Gi+ Pi·Ci
Notes: So what we are going to do actually in the Carry Look Ahead adder is to predict the carry.
We will start from this table truth table, the sum is not mentioned because I have already told you that we are going to focus on the carry output so what we are going to do in this truth table is to see when the carry output is 1 or high and do some analysis.
There are the four cases in which carry output is high. So let's consider the last two cases. In this, you can see that whenever both A and B are high, the carry output is high. It doesn't depend upon your carry input whether it is 0 or 1. So, this is A and B.
The next cases, you can see that CI is always high and one of A and B is high. So, we can say that when A XOR B is equal to 1 and also CI(C input) is equal to 1.
We can write CO(C output) as A and B or A XOR B and CI(C input).
This is we just evaluated from our truth table. Now there are some terminologies involved with this expression. Let me explain you that. This part we call as carry generator and this part we call as carry propagator. Why we call it as carry generator and why we call it as carry propagator? It is because there is no dependency on CI in this first case. The carry is generated depending upon A and B, only in this case the carry is generated. When the carry from the CI is propagated as one so we call it as carry propagator. This part we call it G and this part we call it P depending upon generator and propagator.

## Slide 42: Carry Look Ahead Adder
For multi-bits adder
C1 = G0 + P0C0
C2 = G1 + P1C1
Gi = Ai · Bi
Pi = Ai ⊕ Bi
C3 = G2 + P2C2
… …
Ci = Gi + PiCi = Gi-1 + Pi-1Gi-2 + … + Pi-1Pi-2…P1G0 + Pi-1Pi-2 … P0C0
= G1 + P1G0 + P1P0C0
= G2 + P2G1 + P2P1G0 + P2P1P0C0
∑
∑
∑
B3
A3
B2
A2
B1
A1
B0
A0
C0
∑
C1
C2
C3
P3
G3
P2
G2
P1
G1
P0
G0
Carry look ahead logic
C4
S0
S1
S2
S3
C0
Ci+1 = Gi+ Pi·Ci

## Slide 43: Carry Look Ahead Adder
Fan-in constraint: In practice, the number of inputs of a gate is limited
Cannot directly build carry look ahead adders with a large number of bits
Do it in a hierarchical way!
Ci = Gi + PiCi = Gi-1 + Pi-1Gi-2 + … + Pi-1Pi-2…P1G0 + Pi-1Pi-2 … P0C0
∑
∑
∑
B3
A3
B2
A2
B1
A1
B0
A0
C0
∑
C1
C2
C3
P3
G3
P2
G2
P1
G1
P0
G0
Carry look ahead logic
C4
S0
S1
S2
S3
C0

## Slide 44: Carry Look Ahead Adder
C0
4-bit adder
PI
GI
S3-0
Cout
B3-0
A3-0
∑
∑
∑
B3
A3
B2
A2
B1
A1
B0
A0
C0
∑
C1
C2
C3
P3
G3
P2
G2
P1
G1
P0
G0
Carry look ahead logic
C4
S0
S1
S2
S3
C0
GI = G3+P3G2+P3P2G1+P3P2P1G0
PI = P3P2P1P0

## Slide 45: Carry Look Ahead Adder
C0
4-bit adder
PI0
GI0
S3-0
Cout
B3-0
A3-0
C12
4-bit adder
PI3
GI3
S15-12
Cout
B15-12
A15-12
C4
4-bit adder
PI1
GI1
S7-4
Cout
B7-4
A7-4
C8
4-bit adder
PI2
GI2
S11-8
Cout
B11-8
A11-8
Carry look ahead logic
C4 = GI0 + PI0CI0
C8 = GI1 + PI1CI1 = GI1 + PI1GI0 + PI1PI0CI0
C12 = GI2 + PI2CI2 = GI2 + PI2GI1 + PI2PI1GI0 + PI2PI1PI0CI0

## Slide 46: Multiplexers
Selects binary information from one of many input lines and directs it to the output line
Notes: Multiplexer is a combinational circuit that selects binary information from one of many input lines and directs it to the output line. Here you can see this thing in which there are four inputs and one output and a dialer. It means you can select any input I0 I1 I2 I3 by moving this dialer. At this position the position you can see the output Y is going to be I0 if I move it here at this point then the Y is going to be I2. So you already know that this input lines are having the data the information of some activity and by moving this dialer we can have a particular line carrying a particular information selected has the output Y. We call it simply a data selector because it is selecting our data.

## Slide 47: Multiplexers
Select Line/selector variables
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
S1
S0
4:1 MUX
Notes: How this dialer is moving and how out of these four inputs one of the input is being selected? it is done by a select line or we also call it a selector variable.
When the value of s0 and s1 are 0 0, then the input I0 will be selected an output Y will be I0. Similarly when s1 and s0 are 1 1, the input I 3 is being selected as the output Y.

## Slide 48: Multiplexers
Types
  2:1 MUX 4:1 MUX 8:1 MUX 16:1 MUX 32:1 MUX
Type | Number of select lines
2:1 MUX | 1
4:1 MUX | 2
8:1 MUX | 3
16:1 MUX | 4
32:1 MUX | 5
m
n

## Slide 49: Multiplexers
E | S | Y
0 | X | 0
1 | 0 | I0
1 | 1 | I1
S
E
2:1 MUX
(Enable)
Build a 2:1 multiplexer
Notes: Let's try to study something more about 2 raise to 1 MUX. The one more thing is there in this multiplexer is we call E, which is the enable. Let’s see the truth table for the 2 cross 1 MUX.
When the value of E is equal to zero, this circuit will not work and when the circuit is not working, the output is equal to zero. So whatever the value of select line we don't care it is always going to be zero when the enable is zero.
When the enable is one and S is equal to zero, Y is connected to I0, so Y will be I0 and when S is equal to one, Y is connected to I1 and it is equal to i1.
Let's try to find out the logical expression for this. We will see for this two cases.

## Slide 50: Multiplexers
Build a 2:1 multiplexer
S
E
Y
Notes: So the next thing is the implementation of this circuit. You can easily implement it by using the two and gates.
There are so many uses of these multiplexers. It is a medium scale integrated circuit. And it is available in the form of ICs(integrated circuit). There are different ICs for different types of multiplexers available in the market and by using a single IC you can implement various number of what combinational circuits, like you want to implement a half adder a full adder or subtractor or any other combinational circuit, you can just simply implement it by using a MUX a single IC, you don’t require much gates in that. So there may be great advantages of doing this thing.
So let's see what are the advantages of using the multiplexer. The first advantage is, it reduces the number of wires, I just told you that we don't require number of gates, you are just going to implement your logic your combinational logic by using a single IC. For example if you have to connect ten gates, you require so many wires and if you don't have to connect ten gates you just have to connect one or two gates, then you are going to require lesser number of wires.
The another thing is it reduces the circuit complexity and cost. Let's see how, I just told you that the wires are reduced and wires are reduced because the gates are reduced. When both wires and gates are reduced definitely the complexity is going to reduce and at the same time caused because gates and wires have definitely some cost.
The third point is, implementation of various circuit using the MUX.

## Slide 51: Outline
Combinational logic circuits
Sequential logic circuits

## Slide 52: Sequential Logic Circuits
Combinational logic circuits: output only depends on current inputs
Sequential logic circuits: output depends on both current inputs and history inputs
Sequential logic has state (memory) while combinational logic does not

## Slide 53: SR Latch
SR (set-reset) Latch
  The simplest bistable (stable in set or reset state) device
R
S
Q
Q
-
A | B | Q
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR
Suppose to be always
opposite to each other

## Slide 54: SR Latch
Assume the current state is as follows
  Q=1
R
S
Q
Q
-
1
0
0
0
Notes: The starting state here is that s and R are both low, that is both inputs are 0.
Q is high, that is the output is warm and not Q the inverse of this is 0.
Both of the inputs of the top nor gate are 0. So the output of the top gate is 1. This is exactly what you would expect from an or gate.
The inputs of the lower nor gate are 1 and 0, so the output of the lower gate is 0. Because Q is 1 the latch is currently storing 1.

## Slide 55: SR Latch
R
S
Q
Q
-
1
0
0
0
1
0
0
1
1
Change the input R to 1
  Q becomes 0  “reset” the SR Latch
  Change R back to 0, keep this state
A pulse to R resets SR Latch
Notes: (click)Now we apply a pulse to input R to reset the latch.
This changes the output of the top gate and then this is fed back into the lower gate.
The lower gates output also changes and this is fed back into the top gate.
(click)The pulse that was applied to reset the SR latch is then removed and re zero again.
But the output at Q is now zero so the latch is now storing a zero.

## Slide 56: SR Latch
R
S
Q
Q
-
0
0
0
1
0
1
1
0
0
1
1
Change the input S to 1
  Q becomes to 1  “set” the SR Latch
  Change S back to 0, keep this state
A pulse to S sets SR Latch
Q
S
R
press/release
buttons
Notes: In order to store a 1 again, a pulse must be applied to input S which will set the latch.
(click)again notice how the various changes are propagated around the circuit.
(click) the set pulse is then removed and the circuit is now latched into a set state it's storing a 1 again.
Notice that if another set pulse is applied, it has no effect. Applying a set pulse at S will always force the latch into a set state regardless of the previous state of the latch.
Similarly, applying a reset pulse will always force the latch into a reset state. It should be noted that S and R are never left high, that is neither is ever set continuously to the value 1. The latch is controlled by pulses only.

## Slide 57: SR Latch
Truth table of SR Latch
  When both R and S are 0,
R
S
Q
Q
-
0
0
1
1
0
0
S | R | Q | Q
0 | 0 | 1 0 | 0 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0

## Slide 58: SR Latch
Truth table of SR Latch
  When both R and S are 0,
R
S
Q
Q
-
0
0
0
0
1
1
S | R | Q | Q
0 | 0 | 1 0 | 0 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
  Q is either 1 or 0, depending on the past state

## Slide 59: SR Latch
R
S
Q
Q
-
1
0
0
0
1
1
S | R | Q | Q
0 | 0 | 1 0 | 0 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
Truth table of SR Latch
  When R=1 and S=0, Q=0 (reset)
Notes: Let's examine the truth table as this SR latch is reset again.
The reset pulse is applied. S is 0 R is 1. output Q is 0 and its inverse not Q is 1.The SR latch is storing a 0.

## Slide 60: SR Latch
R
S
Q
Q
-
0
0
0
0
1
1
S | R | Q | Q
0 | 0 | 1 0 | 0 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
Truth table of SR Latch
  When the reset signal to R is removed, Q still remains 0
Notes: The reset pulse is removed. Both S and R are 0 again. Output Q remains at 0 and its inverse remains at 1. The SR latch is still storing a 0.

## Slide 61: SR Latch
R
S
Q
Q
-
0
1
1
0
0
S | R | Q | Q
0 | 0 | 1 0 | 0 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1
Truth table of SR Latch
  When R=0 and S=1, Q=1 (set)
Notes: A set pulse is applied. S is 1 and R is 0. The output Q becomes 1 and its inverse becomes 0.

## Slide 62: SR Latch
R
S
Q
Q
-
0
1
1
0
0
S | R | Q | Q
0 | 0 | 1 0 | 0 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
0
Truth table of SR Latch
  When the set signal to R is removed, Q still remains 1
Notes: The set pulse is removed. S is 0 and R is 0. Output Q is still 1 and not Q is of course 0.

## Slide 63: SR Latch
R
S
Q
Q
-
1
0
0
0
0
S | R | Q | Q
0 | 0 | 1 0 | 0 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1
Truth table of SR Latch
  When R=1 and S=1, both Q and not Q are 0
  Invalid state
Notes: Now the only circumstance we haven't considered is when both inputs S and R are set to 1 at the same time.
If this were to occur, we'd be telling the SR latch to set the value of Q to both 1 and 0 simultaneously.
In reality Q would become 0 and not Q would also become 0.
This would sort itself out if one of the inputs fell to 0 before the other.
For example, if our fell to 0 first, with S still at 1, then Q would become 1 again. If however both inputs are at 1 and both fell to 0 at the same time we have what's known as a race condition between the two gates. They be racing each other to feedback their new output and it’s impossible to know which one would win. Hence if both inputs are high the next state of the latch can't be determined.

## Slide 64: SR Latch
R
S
Q
Q
-
1
0
0
0
0
1
Truth table of SR Latch
  When R=1 and S=1, both Q and not Q are 0
  Invalid state
invalid
S | R | Q | Q
0 | 0 | 1 0 | 0 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
Notes: Now the only circumstance we haven't considered is when both inputs S and R are set to 1 at the same time.
If this were to occur, we'd be telling the SR latch to set the value of Q to both 1 and 0 simultaneously.
In reality Q would become 0 and not Q would also become 0.
This would sort itself out if one of the inputs fell to 0 before the other.
For example, if our fell to 0 first, with S still at 1, then Q would become 1 again. If however both inputs are at 1 and both fell to 0 at the same time we have what's known as a race condition between the two gates. They be racing each other to feedback their new output and it’s impossible to know which one would win. Hence if both inputs are high the next state of the latch can't be determined.

## Slide 65: SR Latch
R
S
Q
Q
-
0
1
1
0
0
S | R | Q | Q
0 | 0 | 1 0 | 0 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1
This is an Active High SR latch
  In most of time, both inputs are 0, a momentarily 1 (high voltage) sets/resets the SR latch
Notes: A set pulse is applied. S is 1 and R is 0. The output Q becomes 1 and its inverse becomes 0.

## Slide 66: SR Latch
R
S
Q
Q
-
0
0
1
1
0
0
S | R | Q | Q
0 | 0 | 1 0 | 0 1
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
S | R | Q | Q
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | 0 1 | 1 0
R
S
Q
Q
-
1
1
0
1
1
0
Invalid
Invalid
Active high SR latch
Active low SR latch
Notes: To summarize them, an SR latch can be built from nor gates or from manned gates.
Both types of latch do the same job but they just controlled in a slightly different way.
The NOR gate based SR latch is set or reset with high logic. That is, it is an active high SR latch.
the NAND gate SR latch on the other hand is set or reset with low logic. That is, it's an active low SR latch.

## Slide 67: SR Latch
R
S
Q
Q
-
S | R | Q | Q
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | 0 1 | 1 0
Active low SR latch using NAND gates
Notes: The wiring of this SR latch is the same but notice that input S is at the top now and R is at the bottom.
(click)Here’s a truth table for this variation of the SR latch. it's a little different from the truth table we've just seen because this latch behaves differently.

## Slide 68: SR Latch
R
S
Q
Q
-
S | R | Q | Q
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | 0 1 | 1 0
1
1
1
0
Active low SR latch using NAND gates
Notes: The difference is that R and S are kept high most of the time.
Here we can see that output Q is zero so the latch is storing a zero.

## Slide 69: SR Latch
R
S
Q
Q
-
S | R | Q | Q
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | 0 1 | 1 0
0
1
0
1
1
0
Active low SR latch using NAND gates
Notes: When input s is made low momentarily, that is when s becomes 0 and R is still 1.
The output at Q becomes warm.

## Slide 70: SR Latch
R
S
Q
Q
-
S | R | Q | Q
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | 0 1 | 1 0
1
1
0
1
1
0
A low-voltage pulse to S sets SR Latch
Active low SR latch using NAND gates
Notes: The latch is now storing a 1 and S can be returned to its normal high state.

## Slide 71: SR Latch
R
S
Q
Q
-
S | R | Q | Q
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | 0 1 | 1 0
1
0
1
0
0
1
Active low SR latch using NAND gates
Notes: When R is set low momentarily, the output at Q is changed to zero.

## Slide 72: SR Latch
R
S
Q
Q
-
S | R | Q | Q
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | 0 1 | 1 0
1
1
1
0
0
1
A low-voltage pulse to R resets SR Latch
Active low SR latch using NAND gates
Notes: R can then return to its normal high value and the latch is now storing a zero again.
An SR latch built from NAND gates like this is more explicitly known as an active low SR latch.

## Slide 73: SR Latch
R
S
Q
Q
-
S | R | Q | Q
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | 0 1 | 1 0
0
0
1
1
1
1
Invalid
Active low SR latch using NAND gates
Notes: An SR latch based on NAND gates also has a forbidden state that is when both S and R are simultaneously 0.
This would result in an illegal state in which both Q and its complement are 1.

## Slide 74: Gated SR Latch
S
E
R
Q
Q
0
0
0
1
1
Can only change state while it’s enabled
  “enabled”: input to the E is 1
Notes: A gated set/reset latch is an SR latch that can only change state while it’s enabled.
For example, imagine an air conditioning system in the building, each room could have its own cooling unit controlled independently by its own SR latch, the set and reset signals might come from a temperature sensor or a humidity sensor in the room. If these were gated SR latches then a central control panel could be used to enable or disable the switching on and off of these units on a room-by-room basis.

## Slide 75: Gated SR Latch
R
S
Q
Q
-
Can only change state while it’s enabled
  “enabled”: input to the E is 1
Notes: Here's an uncoated SR latch.
Remember an SR latch built from nor gates like this one is an active high SR latch.
This means it requires a high pulse that’s a 1 to be applied at input S in order to get a high output at Q, in other words to set the latch.
Alternatively, to reset the latch and make the output at Q 0, it requires a high pulse to be applied to input R.
It's invalid for both S and R to be made high at the same time.
An SR latch is said to be level sensitive, this means it will respond to a valid change in either S or R regardless of the duration of the input pulse.
It's the level high or low that matters not how long it's applied for.

## Slide 76: Gated SR Latch
Can only change state while it’s enabled
  “enabled”: input to the E is 1
R
S
Q
Q
-
E
Notes: To build a gated SR latch, we can make some simple enhancements to an SR latch by connecting a pair of AND gates in series with the inputs of an OR based SR latch.
We've created a third input E which can be used to enable or disable the latching effect.
A regular AND gate will only have a high output if both inputs are high.
So only when E is set to 1 with a 1 from S or a 1 from R get through to our cross connected NOR gates.

## Slide 77
S
E
R
Q
Q
1
0
0
0
0
S
E
R
Q
S
E
R
Q
Q
1
1
0
0
0
S
E
R
Q
Q
1
0
0
0
0
S
E
R
Q
Q
1
0
0
0
1
S
E
R
Q
Q
0
1
0
1
1
S
E
R
Q
Q
0
0
0
1
1
S
E
R
Q
Q
1
0
1
0
1
S
E
R
Q
Q
1
0
0
0
1
S
E
R
Q
Q
1
0
0
0
0
S
E
R
Q
Q
1
1
0
0
0
S
E
R
Q
Q
1
0
0
0
0
S
E
R
Q
Q
1
0
0
0
1
S
E
R
Q
Q
0
1
0
1
1
S
E
R
Q
Q
0
0
0
1
1
S
E
R
Q
Q
0
0
0
1
0
S
E
R
Q
Q
0
0
1
1
0
S
E
R
Q
Q
0
0
0
1
0
Timing diagram
time
Notes: Now let’s examine what happens when E varies.
(click)You can see that some of the time E is high and some of the time E is low.
(click)We begin with an output of 0 but Q, and because E is low the latch is disabled. (click)
(click)S goes high but it has no effect on the output of the latch. (click)
(click)Now E is high the latch is enabled.
(click)So when S goes high so does Q.
(click)And when the S drops to low again the latch stays high,
(click)until such time as R goes high and then Q drops to 0 again. (click)
(click)Now E is zero the latch is no longer enabled.
(click)So if S goes high, it has no effect on queue. (click)
(click)E is high again the latch is enabled.
(click)And so it responds when S goes high, the latch is set again. (click)
(click)E goes to zero, the latch is disabled.
(click)R goes high but Q doesn't drop, it remains in its high state. (click)

## Slide 78: Gated SR Latch
Gated SR Latch can be built by
  Adding two AND gates to active high SR Latch, or
  Adding two NAND gates to active low SR Latch
R
S
Q
Q
-
E
R
S
Q
Q
-
E
In both cases, gated SR Latch is active high

## Slide 79: Gated SR Latch
Gated SR Latch can be built by
  Adding two AND gates to active high SR Latch, or
  Adding two NAND gates to active low SR Latch
We usually use this symbol to represent a gated SR Latch
S
E
R
Q
Q

## Slide 80: Gated D Latch
D
E
Q
Q
0
1
1
1
We can build a gated D Latch based on a gated SR Latch
  Also called a data latch or simply a D latch
    D stands for “data”
Notes: A gated D-latch is a 1-bit memory device. The D stands for data. A gated D-latch is also referred to as a data latch or simply a D latch. We're going to look at how a D latch can be built from a gated SR latch and examine its behavior with a timing diagram.

## Slide 81: Gated D Latch
Based on Gated SR Latch, negating S for R
R
S
Q
Q
-
E
0
0
0
1
1

## Slide 82: Gated D Latch
Based on Gated SR Latch, negating S for R
R
S
Q
Q
-
E
D

## Slide 83: Gated D Latch
A simpler implementation
E
D
Q
Q
-
D
Q
Q
-
E

## Slide 84
D
E
Q
Q
0
1
1
1
D
E
Q
D
E
Q
Q
1
0
0
1
D
E
Q
Q
0
1
1
0
D
E
Q
Q
0
0
1
0
D
E
Q
Q
1
0
0
1
D
E
Q
Q
0
1
1
1
D
E
Q
Q
1
0
0
1
D
E
Q
Q
1
0
0
0
D
E
Q
Q
1
1
0
0
D
E
Q
Q
0
1
1
1
D
E
Q
Q
1
0
0
1
Notes: we‘re interested in the relationship between D E and Q, so here they are on a shared time axis. Not Q is always the inverse of Q, so we haven't included it on this diagram.
(click)At our starting point, E is high, in other words the D latch is enabled, D is low and therefore so is Q.
(click)
(click)When D goes high so does Q.
(click)When D goes low so does Q. You can see that while E is high Q is following D.
(click) (click) (click)
(click) when E goes low, Q is latched. (click)it can’t change so we can see here changes in D and not being reflected in Q.
D at the moment is low, Q is high, but when E goes high again(click), Q reflects D and once again Q is following D.
(click) (click)
(click) On this diagram, we see E go in low again, so Q is no longer following D (click) until of course E goes high again.(click)

## Slide 85: Clocked D Latch
Edge detector
Notes: Consider this combination of logic gates for a moment, and NOT gate with a AND gate. One input of the AND gate is always the inverse of the other.

## Slide 86: Clocked D Latch
1
1
0
0
Edge detector
Notes: This is how you might expect it to behave when we input a 1 into the circuit the inputs of the and gate1 & 0 so the output is 0.

## Slide 87: Clocked D Latch
0
0
0
1
0
Edge detector
Notes: When we input a0 into the circuit the inputs of the and gate are 0 & 1so the output is 0.

## Slide 88: Clocked D Latch
1
1
1
1
Edge detector
Notes: The fact is however that the not gate doesn't invert its input instantly.
When the input transitions from low to high, there’s a very very brief period when the output from the NOT gate is the same as its input. This means that for the same very brief period both inputs of the AND gate high and therefore so is its output.

## Slide 89: Clocked D Latch
1
1
1
0
0
Edge detector
Notes: When the NOT gate catches up everything is once again as we'd expect.

## Slide 90: Clocked D Latch
0
0
0
0
0
Edge detector
Notes: Similarly, when the input transitions from high to low, there's another very brief period in which the NOT gate must catch up but notice that this doesn’t affect the output of the and gate.

## Slide 91: Clocked D Latch
0
0
0
1
0
Edge detector
Notes: What we have here then is a device that can detect the very brief instant at which an input rises from low to high.

## Slide 92: Clocked D Latch
0
0
1
1
1
1
1
1
1
0
1
1
0
0
0
0
0
0
0
0
0
1
C
Output
Edge detector
Raising edge detector
Notes: Let’s examine the operation of this edge detecting circuit on a timing diagram. The top chart shows a clock signal being applied to the input, the lower chart shows the corresponding output. The output of this circuit is low most of the time.
(click)
(click) but you can see that when the input changes from low to high there’s a very brief moment in which the output of the NOT gate lags behind its input. So, momentarily the output of this circuities also high.
We've isolated just the rising edge of the clock cycle what we have here then is a positive edge detection device.

## Slide 93: Clocked D Latch
E
D
Q
Q
-
1
1
1
0
C
Connecting the raising edge detector to a Gated D Latch
Notes: Here is our D latch again.
(click)when we install our edge detection device at E, we can rename the enabling input to C. (click)
see for clock our D latch has been changed from a level triggered device into an edge triggered device. Some people would now call this a flip-flop and by many definitions they'd be correct. A flip-flop being a clock edge triggered by stable which can be in one state or another. Purists however would argue that this is actually a pulse latch but it does now behave something like a flip-flop albeit with some limitations.

## Slide 94: Clocked D Latch
D
C
Q
Q
D
C
Q
Notes: The clocked d-latch has its own symbol notice the addition of a triangle next to input C indicating the dynamic nature of the clock input. So let's analyze its behavior on a timing diagram.
(click)D is sampled whenever there's a rising edge in the clock cycle.
(click)For the rest of the time, the device is latched. Q can’t change so this is what we would expect from an edge triggered D latch some what different from its level triggered counterpart.

## Slide 95: Clocked D Latch
The output pulse of the raising edge detector is instantaneous
If we worry the generated pulse is too short, we can add more delays to generate wider output pulse
C
Output
1
1
0
0
C
Output
0
0
0
1
0

## Slide 96: Clocked D Latch
Falling edge detector
1
1
0
0
1
0
0
0
D
C
Q
Q

## Slide 97: Clocked D Latch
D
Q
Q
-
1
1
0
C
0
Connecting the edge detector to a gated D Latch
  The value of D is sampled at the corresponding edge
Notes: Another enhancement we can make is to add an extra pair of inputs called preset and clear.

## Slide 98: Clocked D Latch
0
D
Q
Q
-
1
1
0
C
PRE
CLR
Adding preset (PRE) and clear (CLR)
Notes: The only thing that's changed here is we're using three input NAND gates now. And as with any NAND gate only when all of the inputs are high is the output low. So when preset and clear are both kept high, they make no difference to the latching behavior.

## Slide 99: Clocked D Latch
D
Q
Q
-
1
0
1
C
0
PRE
CLR
Adding preset (PRE) and clear (CLR)
If CLR is 0 (PRE is 1), Q will fall to 0; (don’t need to wait for the clock edge)

## Slide 100: Clocked D Latch
Adding preset (PRE) and clear (CLR)
D
Q
Q
-
1
1
0
C
0
PRE
CLR
If PRE is 0 (CLR 1), Q will raise to 1 (don’t need to wait for the clock edge)

## Slide 101: Clocked D Latch
Adding preset (PRE) and clear (CLR)
D
Q
Q
-
1
1
0
C
0
PRE
CLR

## Slide 102: D Flip-Flop
Gated D Latch
Gated SR Latch
Notes: let's put the two together

## Slide 103: D Flip-Flop
CLK
D
Q
Q
-
Notes: so that the outputs of the D latch become the inputs of the SR latch.

## Slide 104: D Flip-Flop
CLK
D
Q
Q
-
Notes: now let's connect the inverse of the clock signal to the enabling input of the SR latch. This device is known as a master slave D type flip-flop. With this type of memory device, we can precisely control the moment at which a group of them will change state.
The latch on the left is called the master and the latch on the right is known as the slave.

## Slide 105: D Flip-Flop
CLK
D
Q
Q
-
Notes: The master latch reads the input value at D when the clock signal is high and latches onto it. In fact, this begins to happen at the rising edge of the clock cycle. Meanwhilethe slave is disabled so the new output from the flip-flop as a whole is not available just yet.

## Slide 106: D Flip-Flop
CLK
D
Q
Q
-
Notes: Then when the clock signal falls to low again, the slave is enabled. Data is passed from the master to the slave and is therefore available at the output. A D type flip-flop can be compared to an airlock consisting of two doors which are never open at the same time. The flip-flop as a whole is never fully open, so an input signal can't pass straight through as it does with a simple deal.
The output of the flip-flop occurs during the next phase of the same clock cycle as that in which the input occurred. That is ever so slightly later. The D type flip-flop is therefore sometimes referred to as a delay type flip-flop.

## Slide 107: D Flip-Flop
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
Notes: Let's simplify our diagram and analyze the behavior of a D type flip-flop on a timing diagram.

## Slide 108
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs

## Slide 109
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: Now let’s take a look at Q s the output of the slave and therefore the output of the flip-flop as a whole. Qs follows Qm because the Masters output is the slaves input but more importantly Qs only follows Qm while C is low because the slave is being fed the inverse of the clock signal.

## Slide 110
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: Consider this point in time Qm is changing from low to high but Qs remains low because C is high.
While the flip-flop is responding to a change in its input. Its output remains unchanged. At this point in time however Qs becomes high to follow Qm at the falling edge of the clock cycle. Notice that Qm the Masters output cannot be changed now because C is low. This means that changes to the input of the flip-flop cannot impact on the output at this point.
Also notice that the output of the flip-flop has been delayed by half a clock cycle.

## Slide 111
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: Consider this point in time Qm is changing from low to high but Qs remains low because C is high.
While the flip-flop is responding to a change in its input. Its output remains unchanged. At this point in time however Qs becomes high to follow Qm at the falling edge of the clock cycle. Notice that Qm the Masters output cannot be changed now because C is low. This means that changes to the input of the flip-flop cannot impact on the output at this point.
Also notice that the output of the flip-flop has been delayed by half a clock cycle.

## Slide 112
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: Here the input at D has changed to low as if in readiness for another change to the state of the flip-flop.

## Slide 113
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: When C goes high the output of the master changes but this has no impact on Qs, that is no impact on the output of the flip-flop as a whole the slave isn't listening.

## Slide 114
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: And soon after we see D going high again during the high phase of the clock cycle, but this glitch has no effect on the output of the flop.

## Slide 115
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: At this point we do seek us changing again to follow D while the clock signal is low, but of course the master will ignore any changes in the input while the flip flops in your output is being made available.

## Slide 116
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: Here we see that D has gone high as if to set the state of the flip-flop to high on the next high pulse of the clock. And when the clock goes high, the Masters output Qm follows D.

## Slide 117
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: But now the input falls to low while the clock is high and so does Qm.

## Slide 118
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: So by the time the clock signal forced to low again and the slave is once again responding to changes in its input the flip-flop has ignored yet another glitch.

## Slide 119
D
C
Q
Q
D
C
Q
Q
D
CLK
Qm
Master
Slave
Qs
Q
Q
D
C
Qm
Qs
Notes: What we’ve seen then is that the D type flip-flop effectively ignores any input fluctuations because the master and the slave are enabled on opposite phases of the same clock cycle. The flip-flop accepts input when the clock signal goes high but only gives up the corresponding output when the clock signal falls to low.
To summarize then a D type flip-flop is a 1 bit memory device. Several flip-flops can be combined to build a register or a bank of memory. A D type flip-flop is built by combining two level triggered latches which act as a master and a slave. The output of the master is the input of the slave. A d type flip-flop is safe because it allows sufficient time for propagation delays and therefore time for the inputs to change and settle down without affecting the output. A D type flip-flop does however involve a lot of components compared to say a pulse latch which makes it relatively slow and power-hungry.

## Slide 120: D Flip-Flop
Master and slave enabled on opposite phases of one clock cycle
  More reliable
Effectively edge-triggered sampling
Several flip-flops combined to build registers or memory bank