## Slide 1: EE2000 Logic Circuit Design
Number Systems & Arithmetic

## Slide 2: Outline
1.1 Number Systems
Introduction to decimal, binary, octal, hexadecimal
Conversion between these number systems
1.2 Binary Arithmetic
Representation of negative numbers
Addition and subtraction of binary numbers
1.3 Binary Codes for Decimal Digits
BCD, Gray codes, ASCII
1.4 Parity and Error Correction

## Slide 3: Number Systems
Decimal (base 10)
E.g. 1, 2, 3, 4, 5, … 10, 11, 12, …
Binary (base 2)
  E.g. 000, 001, 010, 011, …
Octal (base 8)
  E.g. 00, 01, 02, …, 07, 10, 11, …17, 20, …
Hexadecimal (base 16)
    E.g. 1, 2, 3, …, 9, A, B, C, D, E, F, 10, 11, …

## Slide 5: Number with radix
Given a number with radix (or base) r (r is usually a positive integer, but not necessarily)
anan-1...a1a0a-1…a-m+1a-m
where ai = x , x (0,1, ... , r ) its decimal value is given by
n: number of digits
r: radix (base)
an : coefficients (digits)
an-1 rn-1 + an-2 rn-2 + … + a2 r2 + a1 r + a0

## Slide 6: Polynomial Form
For decimal number, r = 10
e.g. (7392)10
= 7 x 103 + 3 x 102 + 9 x 101 + 2 x 100
For binary number, r = 2
e.g. (1101.011)2
= 1 x 23 + 1 x 22 + 0 x 21 + 1 x 20 + 0 x 2-1 + 1 x 2-2 + 1 x 2-3
For octal number, r = 8
e.g. (527)8
= 5 x 82 + 2 x 81 + 7 x 80

## Slide 7: Conversion
Binary to Decimal
For binary number, r = 2
e.g. (1101.01)2
= 1 x 23 + 1 x 22 + 0 x 21 + 1 x 20 + 0 x 2-1 + 1 x 2-2 = 8 + 4 + 0 + 1 + 0 + 0.25
= (13.25)10

## Slide 8: Conversion
Decimal to Binary

## Slide 9: Division Method Decimal to Binary
(98)10
98 / 2 = 49 Remainder = 0 0
49 / 2 = 24 Remainder = 1 10
24 / 2 = 12 Remainder = 0 010
12 / 2 = 6 Remainder = 0 0010
6 / 2 = 3 Remainder = 0 00010
3 / 2 = 1 Remainder = 1 100010
1 / 2 = 0 Remainder = 1 1100010
Ans = (1100010)2
LSB, least significant bit
MSB, most significant bit

## Slide 10: Division Method Decimal to Octal /hexadecimal
(611)10
611 / 8 = 76 Remainder = 3 3
76 / 8 = 9 Remainder = 4 43
9 / 8 = 1 Remainder = 1 143
1 / 8 = 0 Remainder = 1 1143
Ans = (1143)8
611 / 16 = 38 Remainder = 3 3
38 / 16 = 2 Remainder = 6 63
2 / 16 = 0 Remainder = 2 263
Ans = (263)16

## Slide 11: Binary Arithmetic

## Slide 12: Signed Number Representation
Negative binary number?
1) Sign-magnitude format
2) Complement format

## Slide 13: Sign-Magnitude Binary
The MSB be a sign bit
  0 means positive “+”
  1 means negative “-”
  For example:
  4-bit system ( +5 = 0101; -5= 1101)
  Last 3 bits used for magnitude

## Slide 14: Problems of Sign-Magnitude
Overflow!!

## Slide 15: Two’s Complement
  4-bit system ( +5 = 0101; -5= 1101) Sign-Magnitude Binary ( +5 = 0101; -5= 1011) Two’s Complement Binary

## Slide 17: Positive to negative conversion
The carry bit can be ignored.

## Slide 18: Negative to positive conversion

## Slide 19: Addition of 2’s complement
The carry bit can be ignored.

## Slide 20: Binary Subtraction
A – B = A + (-B) = A + (2’s complement of B)

## Slide 21: Problem on Addition using 2’s complement
Therefore, the addition of 2’s complement is excellent for (+ve) and (-ve) numbers arithmetic.

## Slide 22: Radix Complement
There are 2 types of complement for any radix-r number system
  r’s complement and (r-1)’s complement
  For n-digit radix-r number system
  The r’s complement number a is rn-a
  The (r-1)’s complement number a is rn-a-1

## Slide 23: Binary Arithmetic
Addition (+)
Subtraction (-)
Multiplication (x)
  Series of addition
Division ()
  Series of subtraction

## Slide 24: Binary Coded Decimal
There are several BCD
  8421 code
  5421 code
  2421 code
  Excess 3 code
  2-of-5 code
  To perform arithmetic operations directly with BCD
When communicating with computer systems
Input: convert decimal no. to binary
Process: perform arithmetic calculations in binary
Output: convert binary result back to decimal
To develop code for human-computer communications
Digits: Binary Coded Decimal (BCD), Gray Code
Alphanumeric: ASCII Code

## Slide 26: 8421 BCD Example

## Slide 27
o.

## Slide 28: Properties of 2421 code
A self-complementing code (9’s complement)
  The complement of 0 is 9 (0000  1111)
  The complement of 1 is 8 (0001  1110)
  The complement of 2 is 7 (0010  1101)
  The complement of 3 is 6 (0011  1100)
  The complement of 4 is 5 (0100  1011)

## Slide 29
o.

## Slide 30: 2-of-5 code
o.

## Slide 31: BCD Summary
Weighted codes
  8421, 5421, 2421 codes
Non-weight codes
  XS3, 2-of-5 code
Self-complement
  2421, XS3 codes
Able to detect error
  2-of-5 code

## Slide 32: BCD Drawbacks
Inefficiency of storage
  For weighted codes and XS3 code
    Used 10 out of 16 combinations
    6 combinations waste
  For 2-of-5 code
    Used 10 out of 32 combinations
    22 combinations wasted
Complex arithmetic calculations

## Slide 33: 8421 Code Addition
o.

## Slide 34: Gray Code
2-bit gray code | 3-bit gray code | 4-bit gray code | decimal
00 | 000 | 0000 | 0
01 | 001 | 0001 | 1
11 | 011 | 0011 | 2
10 | 010 | 0010 | 3
00 | 110 | 0110 | 4
 | 111 | 0111 | 5
 | 101 | 0101 | 6
 | 100 | 0100 | 7
 |  | 1100 | 8
 |  | 1101 | 9
 |  | 1111 | 10
 |  | 1110 | 11
 |  | 1010 | 12
 |  | 1011 | 13
 |  | 1001 | 14
 |  | 1000 | 15
Gray code (after Frank Gray) originally designed to prevent spurious output from mechanical switches.
Today, Gray codes are widely used for error corrections in digital communications such as digital TV and cable TV systems.
One bit difference in the next or adjacent code word independent of the direction taken in the code.

## Slide 35
35
Binary code to Gray code conversion
Place a leading 0 before the MSB.
XOR adjacent bits together starting from the left hand side of this number will result in gray code.
XOR
e.g. 8210 ---> 10100102 00  0
01  1
0 1 0 1 0 0 1 0 10  1
       11  0
1 1 1 1 0 1 1  Gray code

## Slide 36
36
Gray code to Binary code conversion
copy the first 1 starting from left hand side and continue with 1 until the next 1 appears in the gray code.
change to 0 and continue with 0 until the next 1 appears in the gray code.
change to 1 and follow steps (i) & (ii).
10001011  gray code
11110010  binary code

## Slide 37: ASCII Code American Standard Code for Information Interchange
o.

## Slide 38: Code Summary

## Slide 39: Parity and Error Correction
The simplest method for error detection is using parity bit
  An additional bit attaches to the original code
  Two kinds of party bit (even or odd parities)
The value of parity bit is defined by the total no. of “1” in the resulting codeword either even or odd

## Slide 40
o.