## Slide 1: EE3114 Systems and Control 4. Transient and Steady-State Response Analysis
Semester B, 2018-19
2018-9-26

## Slide 2: Framework of Lectures
System
Time Domain Frequency Domain
 Laplace Transform 
State-Space Formulation Frequency Analysis
(dynamic responses,
transients, steady-states,
root-locus, PID controllers)
 mixed 
(State-feedback,
Controllability, controller
Observability, observer
Optimal control)
Today:
Transient and Steady-State Analysis

## Slide 3
Given Transfer Function G(s) and Input U(s):
Y(s) = G(s)U(s)
G(s)
U(s)
Y(s)
Objective of Control :
To obtain a desired output
“Desired” --- described by some “Specifications” for the system output from some common input (impulse, step, ramp)

## Slide 4: Time Response Specifications
Focus: Specifications for Step Response
System
Why?
Impulse Response only “recovers” the Transfer Function and is simple
Ramp Response is complicated but can be treated as a Step Response:
And, similar procedures can be applied to other inputs

## Slide 5: Transient Response Specifications
Rise time tr:
time required for response to rise from 0% to 100% of set-point value for under-damped systems;
time required for response to rise from 10% to 90%of set-point value for over-damped systems;
Settling time ts: time for output to settle within ±δ% of set-point value
For second-order LTI systems
y(t)
Time to reach 50% of set-point value
Set-point value

## Slide 6: Transient Response Specifications
Overshoot Mp: maximum % of output overshooting the set-point value
Peak time tp: time for output to reach max value
tr , ts ,Mp , tp measure the system output responding to the step function
“Fastness” measured by (tr , tp) versus “Nearness” measured by (Mp , ts )
y(t)
For second-order LTI systems
Time to reach 50% of set-point value
Set-point value

## Slide 7
Standard form of a typical second-order system
  (unit step input)
U(s)
Y(s)
For a second-order system, given ωn and ζ
Find: tr , ts ,Mp , tp
(Recall Lecture-3 or Tutorial-4)

## Slide 8
Find Peak Time by = 0 (Maximum via Calculus)
First maximum  Peak time
0
1
Peak time
y
t
%MatLab code
DR = 0:0.01:1;
tp = pi./sqrt(1-DR.^2);
plot(DR,tp);
%axis off;

## Slide 9
Find % Overshoot
where
Percentage of Overshoot:
%MatLab code
DR = 0:0.01:1;
Mp =exp(-DR*pi./(1-DR.^2))*100;
plot(DR,Mp)
ylabel('M_p (%)');

## Slide 10
Y(s)

## Slide 11: Trade-off between Response Fastness and Allowable Overshoot

## Slide 12
Recall:
y(t)
- Settling Time

## Slide 13
Recall:
To estimate Settling Time from envelop of y(t) :
Deviation of y(t) from 1 is the product of
  Decaying exponential
  Sinusoidal function (cosine + sine)
Approximation 
For 0.01 
1% Settling Time:

## Slide 14
Sometimes:
2% Settling Time:
5% Settling Time:
Note:
Settling Time is inversely proportional to the product of damping ratio and un-damped natural frequency
Since is usually determined from the requirement of maximum overshoot permitted, the settling time is determined primarily by
Duration of the transient period, i.e., may be varied by adjusting without changing
For a rapid response, must be large

## Slide 15
To estimate Rise Time tr
Since 
 
%MatLab code
DR = 0:0.01:1;
plot(DR,pi-atan(sqrt(1-DR.^2)./DR)./sqrt(1-DR.^2))
ylabel('t_r\omega_n')
xlabel('\zeta')

## Slide 16
To estimate Rise Time:
Rise Time is typically defined as the time to rise from 10% to 90%
It is approximated as
Clearly, to have a small tr , the must be large

## Slide 17: Step Response: with ζ = 0.2 for ωn = 1 and ωn = 10
does not affect the % overshoot
For the same ζ

## Slide 18: Allowable Region on s-Plane
Recall:
Peak Time:
  Depending only on imaginary part of complex poles
  Specification: 
  Pole pair Allowable Region to satisfy
Im
Re

## Slide 19
Percent Overshoot
  Depending only on
  Specification:
  Let
  
    obtained from figure
    Or, by solving equation
    Pole pair Allowable Region to satisfy
Im
Re

## Slide 20
1% Settling Time:
  Depending only on real part of complex poles
  Specification: 
  Pole pair Allowable Region to satisfy
Im
Re

## Slide 21
Rise time
  Depending only on
  Specification: 
  Pole pair Allowable Region to satisfy
Im
Re

## Slide 22: Allowable Region on s-Plane (delineated all by transient requirements)
Rise Time
Overshoot
1% Settling Time
Composite of all 3 requirements
+
+
=

## Slide 23
Example: Transformation of Specifications to the s-Plane
Find the Allowable Region in the s-plane for the poles of a Transfer Function of a system if its response requirements are: and 1% settling time
Solution:
From Figure ( )
0.6


## Slide 24: System Stability
A stable system is a dynamic system with a bounded response to a bounded input (i.e., bounded input yields bounded output, BIBO), for all time
An asymptotically stable system is a dynamical system with its output converges to zero as time
G(s)
R(s)
Y(s)

## Slide 25
Poles:
Recall: Step Response of Second-Order LTI systems
unit step
asymptotically
BIBO
BIBO

## Slide 26: Stability Condition
For bounded , one requires poles be located strictly inside LHP (not including the boundary) to ensure bounded
System stable if and only if
all poles of G(s) are located inside LHP
(namely, all the poles of G(s) have negative real parts)
G(s)
R(s)
Y(s)
  A system is unstable if any pole has a positive real part, or
  if there are double poles on the imaginary axis
  A system is marginally stable (or marginally unstable)
  if some poles on the imaginary axis, with other poles in LHP

## Slide 27
How to determine if all roots of D(s) are inside LHP, without going through the great trouble of computing the roots?
First Test:
  if some then D(s) has roots inside RHP
  Proof: For illustration, let n = 3 and D(s) has roots
  So, if are all inside LHP, i.e. they have negative real parts, then coefficients of D(s) must be all positive
Determining System Stability

## Slide 28
First Test is only sufficient but not necessary:
First Test
 If not all coefficients of D(s) are positive, then not all poles are inside LHP, namely, there are some roots in RHP
Example:
 D(s) has some roots in RHP
(roots: – 0.675 + j 0.341, – 0.675 – j 0.341, 0.3497)
If are all inside LHP, namely, they have negative real parts, then coefficients of D(s) must be all positive.
But the converse may not be true:
Example:
 D(s) has some roots in RHP
(roots: 0.0395 + j 0.429, 0.0395 – j 0.429, – 1.0791)

## Slide 29: Routh-Hurwitz Stability Criterion
Adolf Hurwitz (1859-1919)
Edward Routh (1831 – 1907)
A necessary and sufficient (if and only if) condition

## Slide 30
Recall: Quadratic Polynomial
Viete Theorem:
The roots and of satisfy:
Roots and Stability
unstable
unstable
unstable
stable

## Slide 31
Put in Table:
a | c
b | 0
 | 0
a | c
b | 0
 | 0
a | c
b | 0
c | 0
a > 0
b > 0
c > 0
no sign change  Viete Thm   stable
a > 0
b > 0
c < 0
sign changes  Viete Thm 
or
 unstable

## Slide 32: Routh-Hurwitz Stability Criterion
Procedure (Routh Test):
Given:
Form Array:
(Routh Table)

## Slide 33
Given:
Form Routh Table: Calculating:
;; …
; ; …

## Slide 34
Row and are directly from coefficients of D(s)
computed from rows and
; ; …
Row computed from rows and
; ; …
and so on, until row
Check: first column of the table:
If all elements are positive, then all roots of D(s) are in LHP
 System is stable
If some elements are negative, then
 System is unstable
# of sign changes in column = # of roots of D(s) in RHP

## Slide 35
Example:
Given:
Solution: Routh Array is
 D(s) has all roots in LHP  System is stable

## Slide 36
Example:
Given:
Solution: Routh Table is
D(s) has roots in RHP  System is unstable
There are 2 sign changes  There are 2 poles in RHP
sign change

## Slide 37
% Verified by Matlab
D = [1 4 3 2 1 4 4];
roots(D)
% 6 roots: -0.8858, -3.2644, -0.6046 + 0.9935i, -0.6046 - 0.9935i,
% 0.6797 + 0.7488i, 0.6797 - 0.7488i (these 2 roots are in RHP)
% To compare step responses when N(s) = 1 and N(s) = s+1, respectively
N1 = 1;
N2 = [1 1];
SYS1 = tf(N1,D)
SYS2 = tf(N2,D)
step(SYS1,SYS2,0:0.01:20)
legend('N(s) = 1','N(s) = s + 1')

## Slide 38: Special Case I: A row has first element = zero but not all elements are zero
D(s) has roots in RHP (including imaginary axis)
This case is unstable, but more detail can be revealed
Procedure:
Replace this first zero by ε > 0
Complete table as before
Let and check the first column again:
  No sign changes  some roots on imaginary axis
  # of sign changes  # of roots in RHP
Note: , where + is important (cannot be )

## Slide 39
Example:
Solution: Routh table is
First column: 2 sign changes  2 poles in RHP
NEW

## Slide 40
% Validation by Matlab,
D = [1 3 2 6 6 9];
roots(D)
% the roots are -2.9043, -0.7046 + 0.9929i, -0.7046 - 0.9929i
% 0.6567 + 1.2881i, 0.6567 - 1.2881i (2 roots in RHP)
%
% To compare step response when N(s) = 1 and N(s) = s+1,
N1 = 1;
N2 = [1 1];
SYS1 = tf(N1,D)
SYS2 = tf(N2,D)
step(SYS1,SYS2,0:0.001:100)
legend('N(s) = 1','N(s) = s + 1')

## Slide 41: Special Case II: One row has all zero elements
D(s) has some roots on imaginary axis or inside RHP
This case is unstable, but more detail can be revealed
Procedure:
Form auxiliary polynomial Q(s) with coefficients from previous row
Use coefficients of to replace the zero row
Complete the Ruth table and check first column again:
  No sign changes  some roots on imaginary axis
  # of sign changes  # of roots in RHP
Note:
  D(s) can be factorized by Q(s):
  Pair of roots of Q(s) are purely real or purely imaginary

## Slide 42
Example:
Solution: Routh array is
No sign changes in first column  all roots have negative real parts except for a pair on the imaginary axis: roots of Q(s) =
NEW

## Slide 43
% To compare step and ramp responses when
% N(s) = 1, N(s) = s+1, and N(s) = s^2+s+1
D = [1 5 11 23 28 12];
N1 = 1;
N2 = [1 1];
N3 = [1 1 1];
SYS1 = tf(N1,D);
SYS2 = tf(N2,D);
SYS3 = tf(N3,D);
t = 0:0.01:10; % Simulation time
subplot(2,1,1);
step(SYS1,SYS2,SYS3,t)
subplot(2,1,2);
lsim(SYS1,SYS2,SYS3,t,t); % Ramp input u = t
legend('N(s) = 1','N(s) = s + 1','N(s) = s^2 + s + 1')
%title('Ramp Response')

## Slide 44
Example:
Solution: Routh array is
There are 2 sign changes in first column  D(s) has 2 roots in RHP
Q
 D(s) has 2 imaginary roots
NEW
Q(s)
dQ(s)

## Slide 45
Example:
Routh Table
One sign change  one pole in RHP

## Slide 46
Application to Control System Analysis
Closed-loop Transfer Function:
Characteristic Equation:
Routh Table:
For stability, all coefficients in first column must be positive  14/9 > K > 0
(when K = 14/9, system is marginally stable, so becomes oscillatory)
Y(s)

## Slide 47
% Matlab plot
K = [1 14/9 2];
t = 0:0.001:50;
for i = 1:length(K);
D0 = conv([1 1 1],[1 2]);
SYS1 = tf(K(i),[D0 0]);
SYS = feedback(SYS1,1);
subplot(length(K),2,(i-1)*2+1);
step(SYS,t);
subplot(length(K),2,i*2);
lsim(SYS,t,t);
%title('Ramp Response');
legend(['K = ',num2str(K(i))],'location','NorthWest');
end

## Slide 48
END