## Slide 1: EE2000 Logic Circuit Design
Registers and Counters

## Slide 2: Outline
  1 Registers - Registers Parallel load, Bidirectional shift Serial Adder, Accumulator
  2 Counters - Asynchronous Counters Ripple counters
  - Synchronous Counters Up-down counters, Modulo counters, Ring counters, Twist Ring counters

## Slide 3: Applications of Flip-Flops
Flip-Flops are basic element of Static Random Access Memory (SRAM) in CPUs, ALUs, microcontrollers.
Shift register is an example of this kind of memories. This includes:
    Parallel loading shift register : can be used for parallel to serial conversion in serial data communication
    Serial in, parallel out shift register: can be used for serial to parallel conversion in a serial data communication system.

## Slide 4: Registers

## Slide 5: Shift Register
Q
e.g. 3bit shift register by D-type FFs
Q0 Q1 Q2
Q Q Q
D D D
Q Q
Din
CLK
serial input, Din and parallel output Q0, Q1 and Q2.
data moves one position to the right on each clock edge.

## Slide 6: Shift Register
Preset and Clear inputs on the FFs can be utilised to provide a parallel data input feature
Data can then be clocked out through Q2 in a serial fashion, i.e., we now have a parallel in, serial out arrangement
This along with the previous serial in, parallel out shift register arrangement can be used as the basis for a serial data link

## Slide 7
Note: PRE’ and CLR’ inputs are not shown in this diagram

## Slide 8
Note: PRE’ and CLR’ inputs are not shown in this diagram
t0
t1
t2
Clk = ↑
Input
Output

## Slide 13: Counters
Many different counters can be designed based on applications.
We shall focus on ripple counters and synchronous counters

## Slide 14: Counters

## Slide 15: Counters

## Slide 16: Ripple Counters
A ripple counter can be made be cascading together negative edge triggered T-type FFs operating in ‘toggle’ mode, i.e., T =1
Q0 Q1 Q2
‘1’ ‘1’ ‘1’
Q Q Q
T T T
Q Q Q
CLK
Note that the FFs are not clocked using the same clock, i.e., this is not a synchronous design.
000
001
010
011
100
101
110
111

## Slide 17
Ripple Counters
CLK
Q0
Q1 Q2
0 1 2 3 4 5 6 7 0
Problems:
-- Outputs do not change at the same time or synchronously.
So hard to know when count output is actually valid.
-- Propagation delay builds up from stage to stage, limiting maximum clock speed before miscounting occurs.
000
001
010
011
100
101
110
111

## Slide 18
Ripple Counters
If you observe the frequency of the counter output signals you will note that each has half the frequency, i.e., double the repetition period of the previous one. This is why counters are often known as dividers
Often we wish to have a count which is not a power of 2, e.g., for a BCD counter (0 to 9).To do this:
  use FFs having a Reset/Clear input
  Use an AND gate to detect the count of 10 and use its output to Reset the FFs

## Slide 19: Synchronous Counters
Synchronous counter overcomes the problems identified with ripple counters.
In a synchronous design
  all the FF clock inputs are directly connected to the clock signal and so all FF outputs change at the same time, i.e., synchronously
  more complex combinational logic is now needed to generate the appropriate FF input signals (which will be different depending upon the type of FF chosen)

## Slide 20: Synchronous Counter
The delays of all FFs are the propagation delays of their own.
It can be used for frequency division.

## Slide 21: Synchronous Counter Design procedures
  Work out the state transition table
  Determine the FF excitation (easy for D-types)
  Determine the combinational logic for generating the required FF excitation from the current states;
    Note: remember to take into account any unused counts since these can be used as don’t care states when determining the combinational logic circuits

## Slide 22
Synchronous Counter Example
Current state Q2Q1Q0
Q' Q' Q'
2 1 0
2 1 0
D D D
Next state
FF
inputs
By inspection,
D0  Q0
Note: FF0 is toggling Also, D1  Q0  Q1
Use a K-map for D2 ,
Q1Q0
00 01 11 10
1
1
0
Q2 1
1 1
Q0.Q2
Q2
Q1
Q0
Q1.Q2
Q0.Q1.Q2
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Use D-type FFs to design a synchronous counter counting 0 to 7.

## Slide 23
Synchronous Counter Example
Q1Q0
0
Q2 1 1 1
1
0
00 01 11 10
1
Q0.Q2
Q2
Q1
Q
Q1.Q2 Q0.Q1.Q2
Q0
So,
D2  Q2.(Q0.  Q1)  Q0.Q1.Q2
D2  Q0.Q2  Q1.Q2  Q0.Q1.Q2
D
Q
Q
CLK
D0
D
Q
Q
Q1
D1
D2
D
Q
Q
Q2
Combinati- onal logic
Q0
Q0
Q1
1
Q
Q2
Q2

## Slide 24: Synchronous Counter Example with JK FF
Using JK FFs and with the minimum number of states to design a counter with counting sequence: 0,4,2,1,6 and repeat.
0
4
6
1
2

## Slide 25
INPUTS |  |  | OUTPUTS
J | K | Qn (Present State) | Qn+1 (Next State)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
INPUTS |  |  | OUTPUTS | REMARKS
J | K | Qn | Qn+1 | States and Conditions
0 | 0 | X | Qn | Hold State condition J = K = 0
0 | 1 | X | 0 | Reset state condition J = 0 , K = 1
1 | 0 | X | 1 | Set state condition J = 1 , K = 0
1 | 1 | X | Q’n | Toggle state condition J = K = 1
Q(n) | Q(n+1) | J | K
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0
JK Excitation Table |  |  | 

## Slide 26
Q(n) | Q(n+1) | J | K
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0
JK Excitation Table |  |  | 
Present |  |  | Next |  |  | FF-A |  | FF-B |  | FF-C | 
A | B | C | A | B | C | JA | KA | JB | KB | JC | KC
0 | 0 | 0 | 1 | 0 | 0 | 1 | X | 0 | X | 0 | X
0 | 0 | 1 | 1 | 1 | 0 | 1 | X | 1 | X | X | 1
0 | 1 | 0 | 0 | 0 | 1 | 0 | X | X | 1 | 1 | X
0 | 1 | 1 | X | X | X | X | X | X | X | X | X
1 | 0 | 0 | 0 | 1 | 0 | X | 1 | 1 | X | 0 | X
1 | 0 | 1 | X | X | X | X | X | X | X | X | X
1 | 1 | 0 | 0 | 0 | 0 | X | 1 | X | 1 | 0 | X
1 | 1 | 1 | X | X | X | X | X | X | X | X | X
All the unused states are treated as don’t care condition.
0
1
2
4
6
0
4
6
1
2

## Slide 29
Summary