## Slide 1: EE3114 Systems and Control 5. Root Locus Analysis and Design
Semester A, 2018-19
2018-10-3

## Slide 2: Framework of Lectures
System
Time Domain Frequency Domain
 Laplace Transform 
State-Space Formulation Frequency Analysis
(dynamic responses,
transients, steady-states,
root-locus, PID controllers)
 mixed 
(State-feedback,
Controllability, controller
Observability, observer
Optimal control)
Today:
Root-locus Analysis

## Slide 3: Recall: Standard form of second-order systems
U(s)
Y(s)
Damping ratio
Un-damped natural frequency

## Slide 4: Review: Allowable Region on s-Plane
Peak Time:
  Depending only on imaginary part of complex poles
  Specification: 
  Pole pair Allowable Region to satisfy
Im
Re

## Slide 5
Percent Overshoot
  Depending only on
  Specification:
  Let
  
    obtained from figure
    Or, by solving equation
    Pole pair Allowable Region to satisfy
Im
Re
(Lectrure-3: Geometric Meaning of Complex Conjugate Poles)

## Slide 6
1% Settling Time:
  Depending only on real part of complex poles
  Specification: 
  Pole pair Allowable Region to satisfy
Im
Re

## Slide 7
Rise time
  Depending only on
  Specification: 
  Pole pair Allowable Region to satisfy
Im
Re

## Slide 8: Allowable Region on s-Plane (delineated all by transient requirements)
Rise Time
Overshoot
1% Settling Time
Composite of all 3 requirements
+
+
=

## Slide 9
Example: Transformation of Specifications to the s-Plane
Find the Allowable Region in the s-plane for the poles of a Transfer Function of a system if its response requirements are: and 1% settling time
Solution:
From Figure ( )
0.6


## Slide 10: What is a Root Locus?
  (A typical unity-feedback control system)
  Characteristic equation:
  Write  
  Plant transfer function (given)
  Control gain
  (to be designed)

## Slide 11: What is a Root Locus?
   as
   as
  Plant transfer function (given)
  Control gain
  (to be designed)
Root Locus is the movement of the roots of
as K: 0 → ∞

## Slide 12
Root Locus of Transfer Function
Example:
%MatLab code
s = tf('s');
sys = (s + 7)/(s*(s + 5)*(s + 15)*(s + 20));
rlocus(sys)
axis([-22 3 -15 15])
This MatLab plot shows all possible closed-loop pole locations for the control gain K: 0 → ∞
Acceptable Region
(left-hand side of curve)

## Slide 13
Root Locus of Transfer Function
Now, design K such that
overshoot less than 5% ( damping ratio )
rise time = 1 second ( )
Not all closed-loop poles on loot locus satisfy design requirements
To determine what part of the locus is acceptable, use MatLab:
%MatLab code
s = tf('s');
sys = (s + 7)/(s*(s + 5)*(s + 15)*(s + 20));
rlocus(sys);
axis([-22 3 -15 15]);
zeta = 0.7;
wn = 1.8;
sgrid(zeta,wn)
MatLab generates a graph (next page)

## Slide 14
MatLab generates this plot:
(Discussions on next two pages)

## Slide 15
The two dotted lines at about 45-degree angle indicate pole locations with ; in between these lines, the poles have (wanted) but outside the two lines (unwanted)
The semicircle indicates poles with ; inside the circle, (unwanted) and outside the circle (wanted)

## Slide 16
For overshoot < 5%, poles should be in between the two dotted lines
For rise time second, poles should be outside the semicircle
All poles in the above locations are in LHP  closed-loop system is stable
Use MATLAB to choose the desired poles on the locus:
%MatLab code
[K,poles] = rlocfind(sys)
(See next page)

## Slide 17
Click at the point where you want the closed-loop pole to be
(for example, the one marked by "+")
You may also select some point within the allowable region, which are not unique but affect response (Recall: Lecture-3)
%MatLab code
s = tf('s');
sys = (s + 7)/(s*(s + 5)*(s + 15)*(s + 20));
rlocus(sys);
axis([-22 3 -15 15]);
zeta = 0.7;
wn = 1.8;
sgrid(zeta,wn);
[K,poles] = rlocfind(sys)

## Slide 18
Now, verify the Step Response:
Use MatLab
%MatLab code
s = tf('s');
sys = (s + 7)/(s*(s + 5)*(s + 15)*(s + 20));
rlocus(sys);
axis([-22 3 -15 15]);
zeta = 0.7;
wn = 1.8;
sgrid(zeta,wn);
K = 600;
sys_cl = feedback(K*sys,1)
step(sys_cl)
The response has overshoot < 5% and rise time second (as required)

## Slide 19
%MatLab code
s = tf('s');
sys = (s + 7)/(s*(s + 5)*(s + 15)*(s + 20));
rlocus(sys);
axis([-22 3 -15 15]);
zeta = 0.7;
wn = 1.8;
sgrid(zeta,wn);
[K,poles] = rlocfind(sys); %No need to enter value, e.g., K=600
sys_cl = feedback(K*sys,1)
step(sys_cl)
Remark:
Use MatLab (no need to enter K value if using command “rlocfind”):

## Slide 20: Typical Pole–Zero Locations and their Root Loci

## Slide 21: More about Root Locus
Design using G(jω), not G(s), with root locus analysis
Transfer Function for sinusoidal input of frequency ω
(containing )
where { pi } and { zi } are poles and zeros of G(s)
y(t) = ?
r(t) = u0 sin (ωt)

## Slide 22
Partial fraction expansion and Inverse Laplace Transform 
y(t) = A1eP1t + … + AnePnt + ejωt + e-jωt
where A0 = (s - jω)Y(s)|s = jω = G(jω)u0/(2j)

y(t) = A1eP1t + … + AnePnt + |G(jω)| u0 sin(ωt + ∠G(jω))
If the poles of G(s) are distinct and located in LHP, then:
For large t , yss(t) = |G(jω)| u0 sin(ωt + ∠G(jω))
Comparing yss(t) to
|G(jω)| is the amplitude scaling factor of yss(t) vs r(t)
∠G(jω) is the phase (angle) shift of yss(t) vs r(t)
r(t) := u0 sin (ωt)
Notes: Euler

## Slide 23: Representation of G(jω)
Polar Plot
All information (magnitude, phase, frequency) in one plot
The imaginary axis separates stable and unstable pole regions

For a given , considering can reveal lots of useful information

## Slide 24: Polar Plots of some typical Transfer Functions (for information only)

## Slide 25
Bode Plots
Present the information in two plots:
  Magnitude: log10|G(jω)| vs log10 ω
  Phase: ∠G(jω) vs log10 ω
Advantages of log-log scale:
  For ω axis to cover a wide frequency range
  For G(jω) = G1(jω)G2(jω)
   log10|G(jω)| = log10|G1(jω)| + log10|G2(jω)|
  ∠G(jω) = ∠ G1(jω) + ∠ G2(jω)
   Bode plots of G
  = Bode plots of G1 + Bode plots of G2
Special dB unit for magnitude plot:
|G(jω)|dB = 20 log10|G(jω)|

## Slide 26
Bode Plot of Transfer Function
of Standard Second-Order System

## Slide 27
Bode Plot of Transfer Function
of Standard Second-Order System

## Slide 28
Minimum-Phase Systems and Nonminimum-Phase Systems
Minimum-Phase Transfer Functions
Minimum-Phase Systems
They have no poles and no zeros in RHP
 They are stable, and inverses are stable
Nonminimum-Phase Transfer Functions
Nonminimum-Phase Systems
They have either poles or zeros in RHP
Magnitude:
Phase:

## Slide 29
Example:
Draw the Bode plot of the Transfer Function
Solution:
Log-magnitude:
Phase angle:

## Slide 30
L = 0.5
T = 1
Log-Magnitude
_______
Phase

## Slide 31
Bode Plots by MatLab
Example:
Transfer Function (containing
%MatLab code
num = [25];
den = [1 4 25];
bode(num,den);
grid

## Slide 32
Example:
%MatLab code
num = [9 1.8 9];
den = [1 1.2 9 0];
bode(num,den);
grid

## Slide 33: Stability Analysis with G(jω)
s  jω

G(s)  G(jω)

## Slide 34: Stability Analysis with G(jω)
Y(s)
Closed-loop system stability if and only if all poles are located in LHP
Nyquist Stability Criterion:
If (i) G(s)H(s) has P poles in RHP
(ii) constant
then, for closed-loop stability, as , locus must encircle the point for P times counterclockwise
gives all poles 
 the point is important (write: )

## Slide 35
(1) If , for the closed-loop to be stable: “locus must encircle the point for P times counterclockwise”
 (i.e., N + P = 0) 
(2) If , for the closed-loop to be stable: “locus must encircle the point for times counterclockwise”
Remark
Recall: Nyquist Condition A (i): G(s)H(s) has P poles in RHP
For the closed-loop to be stable, one must have N + P = Z
Nyquist Stability Criterion B:
= number of clockwise encirclements of the point –1+j0
( = number of counterclockwise encirclements)
= number of poles of G(s)H(s) in RHP
= number of zeros of 1+G(s)H(s) in RHP
All other cases: namely, otherwise, closed-loop is unstable

## Slide 36
Example:
Nyquist Plot 
Point is encircled by the curve once (P = 1) counterclockwise

Closed-loop system with Transfer Function
is stable
(ii) (constant)
(i) has one pole in RHP

## Slide 37
Example:
Transfer Function
There are no poles of G(s)H(s) in the RHP, so P = 0, and the point is not being encircled counterclockwise, so N = 0,
 Z = 0 = N + P
 Closed-loop system is stable
%MatLab code
num = [1];
den = [1 0.8 1];
nyquist(num,den)

## Slide 38
Example:
If is unknown, but and , and Nyquist plots are obtained as for the following two cases of
Without encirclement
With encirclement(s)
N + P = Z
N + P Z
 can change the system stability

## Slide 39
If the locus passes through the point , then closed-loop poles are located on the imaginary axis
This is marginally stable and is not desirable for practical control systems, so it should be found out, and then be avoided by appropriately designing the control gain K
Common Case:
(Consider only)
 It is very important to know the “margin” of the control gain

## Slide 40: Gain Margin
Definition: Gain Margin (GM) is the maximum scalar factor multiplying to KG(jω) for which polar plot is still not encircling ()
Let polar plot cut real axis at point A (),
-d
A

## Slide 41: Phase Margin
B
Definition: Phase Margin (PM) is the maximum clockwise rotation of polar plot (about the origin), which is still not encircling ()
Draw a circle of radius 1 about the origin and mark the intersection point as point B
PM = ∠
)

## Slide 42: GM and PM from Bode Plot
Point A occurs at point where phase =
Point B occurs at point where magnitude = 1 = 0 dB
B
A
A
A
B
B

## Slide 43: GM and PM from Bode Plot
Gain Margin (GM) is the difference between the magnitude curve and 0dB at the point corresponding to the phase of -180 degree
Phase Margin (PM) is the difference between the phase curve and -180 degree at the point corresponding to the gain of 0dB
B
A
-180
Example:
%MatLab code
bode(50, [1 9 30 40])

## Slide 44
Same Example
%MatLab code
margin(50,[1 9 30 40])
Pm 
 Gm
( W = )

## Slide 45
Example:
A occurs at point where phase =
B occurs at point where magnitude = 0 dB
GM 32.5 dB
()
PM
()

## Slide 46
Special Cases:
G(s)H(s) has poles and/or zeros on the imaginary axis
Example:
It has one pole at 0 (on the imaginary axis)
When , let the pole be with and Then
As , on has , so that
So, locus does not encircle
 The closed-loop system is stable

## Slide 47
END