## Slide 1: CS2115 Computer Organization 2023/2024 Sem A
Chapter 7: I/O System
Dr. Nan Guan
Department of Computer Science
City University of Hong Kong

## Slide 2: Peripheral Devices (I/O Devices)
Peripheral devices include :
    Display peripherals - Video Display (Monitor)
    Input peripherals - Keyboard, Mouse, Tracker ball, Joystick
    Hardcopy peripherals – Dot Matrix and Laser Printers
    …

## Slide 3: Peripheral Devices (I/O Devices)
The structure of a personal computer is to utilize a single bus to connect the CPU, memory, and I/O devices
Each I/O device requires a device controller:

## Slide 4: Communication Interface
Examples
RS-232 serial cable connection
The Universal Serial Bus (USB)
  a simple, low-cost, and easy to use interconnection system
HDMI, VGA: video data interface
Communication interface between two digital systems that transmits data as a series of voltage pulses down a wire.

## Slide 5: Northbridge and Southbridge
Northbridge: memory controller
Southbridge: I/O controller

## Slide 6: I/O Controller (I/O Module)
Major Functions:
Provide a standard interface for I/O operations.
Tailored to specific I/O devices and its interface requirements

## Slide 7: I/O Controller Diagram
Data
Linea
Address Lines
Control
Lines
Data Registers
Status/Control Registers
I/O
Logic
External
Device
Interface
Logic
External
Device
Interface
Logic
Data
Status
Control
Data
Status
Control
. . .
Interface to System Bus or I/O Controller
Interface to External Device

## Slide 8: External Interface
The external interface, must be tailored to the nature and operation of the peripheral
    Parallel vs. serial data transfers
    Data format conversions
    Transfer rates
    Number of devices supported

## Slide 9: External Device
Three types of signals
Control Signals
Status Signals
Data

## Slide 10: I/O Addressing
Memory mapped I/O
Devices and memory share same address space
I/O looks just like memory read/write
No special commands for I/O
Isolated I/O
Separate address spaces
Need I/O or memory select lines
Special commands for I/O

## Slide 11: I/O Techniques
Three techniques for I/O Operations
    Programmed I/O
    Interrupt driven I/O
    Direct Memory Access (DMA)

## Slide 12: Programmed I/O
CPU issues I/O commands to I/O modules and directly controls I/O
Sensing status
Read/write commands
Transferring data
Periodically poll I/O modules to check their status
Disadvantages:
CPU waits for I/O module to complete operation
Waste CPU time – CPU is slowed down to the speed of peripherals
Advantages:
Simple
No extra hardware support required

## Slide 13: Interrupt-Driven I/O
Interrupt-driven I/O:
  To reduce the time CPU spends on I/O operations
CPU issues I/O commands to I/O module
CPU continues for its other tasks while the module
performs I/O operations
The module signals the CPU when I/O operations are finished (Interrupt)
CPU responds to the interrupt by executing an interrupt service routine
CPU recognizes and responds to interrupts at the end of an instruction execution cycle

## Slide 14: Interrupt-Driven I/O
How to identify which device issues the interrupt?
How to decide which one to proceed if multiple interrupts occurs?
Separate Interrupt Lines
  Different device trigger different interrupt lines
Pooling
  Use software to check the status of different devices
Priority control
  Assign priorities to different devices; automatically arbitrated

## Slide 15: Direct Memory Access (DMA)
Interrupt driven and programmed I/O require CPU involvement for I/O operations
DMA (Direct Memory Access) does not need CPU except for initialization of I/O operations
Large amounts of data can be transferred between memory and the peripheral without severely impacting CPU performance
Data lines
Data
count
Control
logic
Data
register
Address
register
Address lines
Request to DMA
Acknowledge from DMA
Interrupt
Read
Write

## Slide 16: Direct Memory Access (DMA)
Interrupt-driven and programmed I/O require CPU involvement for I/O operations
DMA (Direct Memory Access) does not need CPU except for initialization of I/O operations
Large amounts of data can be transferred between memory and the peripheral without severely impacting CPU performance